## Slide 1: CMS Calorimeter Trigger Upgrades
Andrew Rose – Imperial College, London
on behalf of the CMS Level-1 trigger collaboration

## Slide 2: Overview
So many triggers, so little time
Hardware for upgrades
Time-multiplexed triggering
Status of the TMT concept
Firmware
Conclusions

## Slide 3: So many triggers, so little time

## Slide 4: The CMS Calorimeter Trigger
Mitigate risk by building upgrade in parallel:
Current system, albeit modified, remains operational in parallel
TDR upgrade
  All inputs in optical format
  Full tower-level information available in processor cards
Interim trigger for 2015
    Improve processing of existing RCT
  Backup solution for 2015 running
  For use if the current trigger cannot cope and full upgrade not yet available
ECAL
energy
HCAL
energy
HF
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
e/γ
Jets
Existing hardware

## Slide 5: Recommissioned existing trigger
  oRM
  oSLB
  oRSC
ECAL
energy
HCAL
energy
HF
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
e/γ
Jets
Existing hardware
New hardware

## Slide 6: TDR trigger upgrade
ECAL
energy
HF
energy
Calorimeter Trigger
Layer 1
Calorimeter Trigger
Layer 2
HCAL
energy
Existing hardware
New hardware
  oRM
  oSLB
  oRSC
Tower-level granularity data

## Slide 7: Interim (back-up) trigger for 2015
  oRM
  oSLB
  oRSC
ECAL
energy
HCAL
energy
HF
energy
Regional Calorimeter Trigger
Interim Calorimeter Trigger
Finer granularity data
Existing hardware
New hardware

## Slide 8: Schedule
The schedule for the calorimeter trigger upgrades is defined in the TDR:
Slice-test of the TDR trigger design – July 2014
All hardware installed at P5 – November 2014
Commissioning in parallel with the existing trigger – 2015
Fully commissioned and operational – January 2016
The interim trigger for 2015 has a deadline for the completion of commissioning of 31st March 2015

## Slide 9: Hardware for upgrades

## Slide 10: oSLB and oRM
ECAL
energy
HCAL
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
HF
energy
oSLB
oRM

## Slide 11: oSLB and oRM
Kintex-7 FPGAs
Mount on existing VME cards, replacing copper links
Have now been manufactured
Installation pending an installation readiness review
oSLB @ 4.8Gb/s
oSLB
oRM

## Slide 12: μHTR
ECAL
energy
HCAL
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
HF
energy

## Slide 13: μHTR
2× Virtex-6 FPGAs
Cost-optimised
One-for-one replacement of existing HTR cards
Modular design with services on mezzanine cards
Mixed PPod and SFP+ optics

## Slide 14: oRSC
ECAL
energy
HCAL
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
HF
energy

## Slide 15: oRSC
Kintex-7 FPGA
VME interface card
Fits in current RCT crates
18 cards in total
Provides RCT output in optical format to:
  Existing GCT Leaf cards
  Interim trigger processor
Waiting on integration tests before final manufacturing ordered
ECL
to
LVTTL translators
RCT
Clock Interface (NECL)
Avago MiniPOD
Tx Modules
Spartan-6
VME Interface
Kintex-7
XC7K355T
FPGA

## Slide 16: TDR trigger upgrade
ECAL
energy
HF
energy
Calorimeter Trigger
Layer 1
Calorimeter Trigger
Layer 2
HCAL
energy
University of Wisconsin
CTP7

## Slide 17: CTP7
Based on Virtex-7 XC7VX690T FPGA
Zynq processor running Xilinx PetaLinux for service tasks
Baseline Layer 1 hardware
Backplane communication on Ports 12-15 & 17-20 for use with semi-custom VT894 crate
    Auxiliary power connector on front-panel
    Custom-designed heatsink
    Two prototypes in hand
36Tx+36Rx links on 3 CXP modules
12Tx+31Rx links on MiniPODs
Heat Sink

## Slide 18
1.8Tb/s optical signal processor
72Tx+72Rx links at 12.5Gbps
Xilinx Virtex-7 FPGA:
  XC7VX485T or XC7VX690T
On-board firmware repository
2×144Mbit 550MHz QDR RAM
Been in hand for nearly two years
  Continuous testing over that period
  Very well understood
Extensive software and firmware
Currently in manufacture, formally procured through CERN purchasing
10 Gbps
12.5 Gbps

## Slide 19: An observation…
With the recent up-turn in the global economy, many boards which have gone out for manufacturing recently are suffering long lead-times on components!
Manufacturing, testing and installation schedules need to take this into account!

## Slide 20: Time-multiplexed triggering

## Slide 21: Conventional trigger
Conventional Trigger
Data is processed in regions
Boundaries between regions must be handled by sharing or duplicating inputs
Volume of data reduced at each stage by selecting and discarding candidates
When volume of data has been sufficiently reduced it can be passed to the global trigger

## Slide 22: Time-multiplexed trigger
Time-Multiplexed Trigger
Data from an event is buffered and retransmitted to the first processing node over N bunch crossings
Data from the next event is buffered and retransmitted to the second processing node, again, over N bunch crossings
Process is repeated in round-robin fashion across ≥N processing nodes
Because both algorithm latency and data volume are constant, dataflow is fully deterministic and no complex scheduling mechanism is required

## Slide 23: Why TMT?
The Time-multiplexed architecture allows all data to arrive in geometric order:
  Towers at given φ always occupy the same bits on the same optical links
  Towers arrive in order of increasing |η|
This converts a 2D geometric problem to a 1D problem
This allows all algorithms to be fully pipelined†:
  The processing is localised
  Fan-outs reduced
  Routing delays minimised
  Register duplication eliminated
  Also only need to develop one FPGA design
†That is, pipelined at the full data rate, not at the bunch-crossing rate

## Slide 24: Status of the TMT concept

## Slide 25: Status of TMT: Integration test @ B904
MP7’s used here as PP’s
PP-B
PP-T
MP
Demux
Simulating half of the PP cards with a single MP7
Simulating half of the PP cards with a single MP7
oSLB
uHTR
TPG input to PP not part of test
Test set-up @ 904

## Slide 26: Status of TMT: Integration test @ B904
PP - T
PP - B
MP
DEMUX
720 Gbps of data going through the MP board
The MP is processing data from the entire calorimeter

## Slide 27: Status of TMT: Algorithms
All algorithms operate on tower-level information at 240MHz
Compact objects – e/γ/τ
  Use the 2×2 Wisconsin clustering algorithm
  Baseline algorithm currently in CMSSW
Extended objects – Jets
  Use an 8×8 tower circular jet
  Equivalent to cone jet (r=0.35)
  Other algorithms available
Global objects – Ring sums
  Use full granularity equivalent of what is done in current trigger

## Slide 28: Status of TMT: Results
Random data passed through an emulator was used in the testing of the algorithms
Data injected into PP
Time-multiplexed
Optical Fibre
Clustering algorithm (2x2)
Sort
Capture
Compared emulated results (solid line) with those from the MP7 (markers): C++ emulator and hardware match precisely
System latency lower than TDR prediction
No link-errors, no CRC-errors and maintained alignment after a week of operation

## Slide 29: Lessons learned from test
Floor-planning
  Huge impact on algorithm design
  Structure the algorithm to map optimally onto the FPGA
  Reduces risk that after many hours of routing 6 million nets just 1 or 2 fail to meet timing - exceedingly annoying
  Significant timing improvement
  Only viable if signals remain relatively local
Full pipelining of algorithms is essential - even relatively innocuous looking fan-outs in chips this large have the potential to kill off the entire design
uHAL and IPbus are working well, and have made debugging and multi-user crate access both possible and easy
AMC13 has worked extremely well for us during the test

## Slide 30: Firmware

## Slide 31: Firmware
MP7 is a completely generic optical-stream processor
Being used in at least 5 roles in the CMS trigger upgrades
  Interim trigger processing hardware
  TDR trigger processing hardware
  Drift-Tube Track-Finder
  Global Muon Trigger
  Global Trigger
Having common hardware platform obviously helps with maintainability
How to collaboratively develop firmware is not a trivial problem!

## Slide 32: “Base Firmware” Concept

## Slide 33: Implementation Status
Done & Tested
in B904
Done & Tested in B904
Development with BU
Work in
progress
(Dasgupta)
Done & Tested in B904
Done & Tested in B904
Done & Tested in B904
(development of new algorithms is ongoing)

## Slide 34: Floorplan of FPGA: Integration Test

## Slide 35: Floorplan of FPGA
Communication
DAQ
(work in progress)
Clusters
Towers
Jets
Sorting
MGTs and DAQ buffers
MGTs and DAQ buffers
Algorithms

## Slide 36: Resource usage of FPGA
Resource | Fraction of Entire FPGA |  | Fraction of Algorithm Area used
 | Used for infrastructure | Used for algorithm + infrastructure | 
Registers | 9% | 21% | 20%
LUTs | 19% | 36% | 35%
DSPs | 0% | 8% | 13%
BRAM | 12% | 12% | 0%
All Algorithms and Infrastructure:
7 hour build-time
Much better than the >24 hours reported elsewhere

## Slide 37: Software

## Slide 38: IPbus/uHAL
IPbus and uHAL, which are supported as part of the UK calorimeter trigger upgrade program, have been widely adopted outside its original scope
A very large effort has gone into optimization & reliability over the last year:
  Read/write bandwidths both now exceed 0.55Gbps
  Retry mechanism works perfectly on networks with 10% packet loss. Mechanism should work identically for higher loss rates.
University of Wisconsin have a preliminary TCP implementation for embedded processors (e.g. ZYNQ)
Bandwidth tests show rates of 3-4MB/s (0.024-0.032Gbps)
IPbus 2.0 – 01/13
IPbus 2.2 – 01/14
~2.5 FTEs
Plots courtesy of T. Williams

## Slide 39: SoftWare for Automating conTrol of Common Hardware
IPbus and uHAL have rationalized hardware access
Can we rationalize board control S/W?
    MP7, CTP7, MFT7 are all very similar
    One software class to control them all?
Can we use the same software model for production and testing?
    Standardize the concept of 'test‘
    (what goes in, what goes out)
    Introduce flexible system-wise tests:
    from {system A, buffer X} to {system B, buffer Y}
    Requires rationalizing DAQ, data-packing and data-unpacking!
serdes
Algorithm(s)
serdes
buffer
buffer
control
memory
DAQ
input links
output links
L1 System
SubSystem
Board
Control Functions
API
API
API
Hardware
uHAL
Exposable via network interface
Common across L1
Write once and reuse everywhere
Subsystem specialisation
Above: Common Board Model, Below: System Model

## Slide 40: Conclusions

## Slide 41: Conclusions
All hardware for the CMS Calorimeter Trigger upgrade now in hand, albeit having undergone varying degrees of testing:
  TDR upgrade: μHTR, oSLB, oRM, CTP7, MP7
  Interim trigger for 2015: oRSC, MP7
The baseline architecture is a Time-Multiplexed Trigger
The Time-Multiplexed Trigger Integration test at B904 last September was a great success
Many lessons were learned which reaffirmed the motivations for choosing the TMT architecture over a conventional architecture
Have developed a model for collaborative development of firmware
uHAL and IPbus v2 work very well and are being widely adopted outside their original scope