## Slide 1: Triggering at the LHC: Past, Present & Future
Andrew Rose

## Slide 2: Acknowledgement
My thanks to Maxeler Technologies who are sponsoring my participation at HPSP14

## Slide 3: Overview
The CMS experiment
  The challenge
The CMS trigger – conceptually
The CMS trigger – Run 1: The Past
  What is it?
  Lessons which (should) have been learned
Time-multiplexing & Spatial Pipelining
The CMS trigger – Run 2: The Present
  Current state of the system
The CMS trigger – Run 3: The Future
  When “Big Data” really means Big Data

## Slide 4: The CMS experiment

## Slide 5: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~83k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers

## Slide 6: The CMS detector
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~83k PbWO4 Ecal Crystals
≡ 40 TBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
Data rates with no zero-suppression

## Slide 7: The Internet: Visualizing big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr

## Slide 8: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS Raw

## Slide 9: The CMS detector
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~83k PbWO4 Ecal Crystals
≡ 40 TBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
Data reduction
Zero suppression
Analogue Pipelines
Selective Readout
Zero suppression

## Slide 10: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
CMS Raw
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS Zero-suppressed

## Slide 11: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
CMS Raw
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS Zero-suppressed
Tape storage
Five orders of magnitude

## Slide 12: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
CMS Raw
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS Zero-suppressed
Tape storage
Five orders of magnitude
A man is too apt to forget that in this world he cannot have everything.
A choice is all that is left him.
Harry Mathews (1930-present)

## Slide 13: The CMS trigger

## Slide 14: The CMS trigger – Run 1
Throw away 399/400
Throw away 999/1000
Level-1 Trigger (L1T)
Higher-Level Trigger (HLT)
Tape Storage

## Slide 15: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
CMS Raw
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS L1T Input
Tape storage
CMS HLT Input
No tracking
Reduce Ecal resolution

## Slide 16: The CMS Level-1 trigger
CALORIMETER
TRIGGER
MUON
TRIGGER
195,000 DT channels
210,816 CSC channels
162,282 RPC channels
GLOBAL
TRIGGER
128 path Boolean logic tree
61,200 barrel crystals
21,528 endcap crystals
O(104) HCAL channels
8 e/γ candidates
4 τ candidates
8 jets candidates
Energy sums
4 muon tracks
Keep or Discard

## Slide 17: The CMS Level-1 trigger
CALORIMETER
TRIGGER
MUON
TRIGGER
195,000 DT channels
210,816 CSC channels
162,282 RPC channels
GLOBAL
TRIGGER
128 path Boolean logic tree
61,200 barrel crystals
21,528 endcap crystals
O(104) HCAL channels
8 e/γ candidates
4 τ candidates
8 jets candidates
Energy sums
4 muon tracks
Keep or Discard
3.2µs

## Slide 18: Example: Muon Event

## Slide 19: Example: Muon Algorithm
Join the dots
  In 3D
  In 2Tesla magnetic field (outside solenoid) – curved tracks
Remove duplicate candidates
Sort candidates

## Slide 20: Example: Electron/Photon Event

## Slide 21: Example: “Simple” e/γ/τ Algorithm
Form 2x2 sums & filter to prevent multiple counting
Calculate energy-weighted position within cluster
Pileup estimation and pileup subtraction
Classify cluster based on E & H components
Count clusters over threshold for surrounding 8x8 region (isolation)
Select e/γ/τ candidates from generic clusters based on the above criteria
Sort the candidates per ring around the detector
Sort the candidates along the detector

## Slide 22: Example: Jet Event

## Slide 23: Example: Jet Algorithm
<
<
<
<
<
<
<
<
≤
<
<
<
<
<
<
<
≤
≤
<
<
<
<
<
<
≤
≤
≤
<
<
<
<
<
≤
≤
≤
≤
C
<
<
<
≤
≤
≤
≤
≤
≤
<
<
≤
≤
≤
≤
≤
≤
≤
<
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
≤
<
<
<
<
<
<
<
<
≤
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
9×9 jet at tower-level resolution
9×9 sum of trigger towers at every site
Fully asymmetric jet veto calculation
Local Pile-up estimation
Full overlap filtering
Pile-up subtraction
Sort the candidates per ring around the detector
Sort the candidates along the detector

## Slide 24: The CMS trigger – Run 1: The Past

## Slide 25: Run-1 Trigger Architecture: Conventional
Conventional Trigger Architecture
Data is processed in regions
Boundaries between regions must be handled by sharing or duplicating inputs
Volume of data reduced at each stage by coarsifying data or by selecting and discarding candidates
When volume of data has been sufficiently reduced it can be passed to the global trigger

## Slide 26: The CMS Level-1 trigger – Run 1

## Slide 27: Run 1: Processing Platform

## Slide 28: Run 1: Link standards

## Slide 29: The CMS Level-1 trigger – Run 1
Regional Calorimeter
Trigger
Global Calorimeter
Trigger

## Slide 30: The CMS Level-1 trigger – Run 1
CSC
Trackfinder
DT Trackfinder
(aka the green salad)
RPC
Pattern Comparator

## Slide 31: The CMS Level-1 trigger – Run 1
Global
Trigger

## Slide 32: The CMS Level-1 trigger – Run 1
It works! It contributed to the finding of the Higgs Boson
It has been very reliable
Pros

## Slide 33: The CMS Level-1 trigger – Run 1
The inhomogeneity of the links and hardware meant that whenever a change was required during construction, new hardware was required
The number of different board-types means that there is really only one expert per board
Each piece of hardware requires different software. How these operate together was added as an after thought
No software or firmware reuse: Maintainability nightmare
It works! It contributed to the finding of the Higgs Boson
It has been very reliable
Pros
Cons

## Slide 34: The CMS Level-1 trigger – Run 1
The inhomogeneity of the links and hardware meant that whenever a change was required during construction, new hardware was required
The number of different board-types means that there is really only one expert per board
Each piece of hardware requires different software. How these operate together was added as an after thought
No software or firmware reuse: Maintainability nightmare
Lessons which (should) have been learned
Cons
Build a homogenous system
Build a homogenous system
Think about the system (rather than the components) from the start
Build a homogenous system

## Slide 35: So why did CMS end up with such a diverse system?
Boundary-handling
  In a conventional trigger architecture, data is processed in regions and the boundaries between regions require very different handling for a calorimeter subsystem than, say, a muon subsystem

## Slide 36: So why did CMS end up with such a diverse system?
Boundary-handling
  In a conventional trigger architecture, data is processed in regions and the boundaries between regions require very different handling for a calorimeter subsystem than, say, a muon subsystem
Mindset
  There is a mindset that the trigger is a “hardware problem”
  This was true in the past but not really true now
  There is a mindset that software and firmware “come for free”

## Slide 37: So why did CMS end up with such a diverse system?
Boundary-handling
  In a conventional trigger architecture, data is processed in regions and the boundaries between regions require very different handling for a calorimeter subsystem than, say, a muon subsystem
Mindset
  There is a mindset that the trigger is a “hardware problem”
  This was true in the past but not really true now
  There is a mindset that software and firmware “come for free”
Organizational
  Building the trigger was approached like building the detector
  The system was divided into chunks first and the interfaces between chunks decided internally by the groups on each side of the boundary.
  Within each chunk, the group was free to come up with any solution that worked (see above)

## Slide 38: So why did CMS end up with such a diverse system?
Boundary-handling
  In a conventional trigger architecture, data is processed in regions and the boundaries between regions require very different handling for a calorimeter subsystem than, say, a muon subsystem
Mindset
  There is a mindset that the trigger is a “hardware problem”
  This was true in the past but not really true now
  There is a mindset that software and firmware “come for free”
Organizational
  Building the trigger was approached like building the detector
  The system was divided into chunks first and the interfaces between chunks decided internally by the groups on each side of the boundary.
  Within each chunk, the group was free to come up with any solution that worked (see above)
That is simple, my friend. It is because politics is more difficult than physics
Albert Einstein, 1946
Progress is impossible without change, and those who cannot change their minds cannot change anything
George Bernard Shaw (1856-1950)

## Slide 39: Time-Multiplexing & Spatial Pipelining

## Slide 40: Time-multiplexed trigger
Time-Multiplexed Trigger Architecture
Data from an event is buffered and retransmitted to the first processing node over N bunch crossings
Data from the next event is buffered and retransmitted to the second processing node, again, over N bunch crossings
Process is repeated in round-robin fashion across ≥N processing nodes
Because both algorithm latency and data volume are constant, dataflow is fully deterministic and no complex scheduling mechanism is required

## Slide 41: Time-multiplexed trigger
Layer 1
“Preprocessors”
Layer 2
“Processing nodes”
The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue this is a decided disadvantage.
Daniel Slotnick, 1967

## Slide 42: The advantages of Time-Multiplexing
Take the principle to its limits: Eliminate the boundaries completely
No specialization of hardware for a particular boundary handling situation
  “One-board-fits-all” design
No duplication of data needed
  Less hardware and fewer links for a given resolution
No data needs to be thrown away
  Should allow better physics
Equality of data
  Without duplication, all data is equal
  Can easily add new input sources
    Scalability

## Slide 43: The advantages of Time-Multiplexing
But there is nothing to say that we have to go to that extreme…
We could use Time-Multiplexing to reduce a two-dimensional boundary handling problem to a one-dimensional boundary handling problem
Conventional Boundary Handling
Partial TMT
Boundary Handling

## Slide 44: Further advantages of a TM trigger
advantages of a TM trigger?
Architecture is naturally matched to processing of data in FPGAs
  Parallel streams with pipelined steps at data link speed
  Put to great use in the calorimeter trigger
    Reduces a 2D problem down to operations in a single dimension or localised 2D operations

## Slide 45: Spatial Pipelining
Because data is buffered in a Time-Multiplexed Trigger and reordered for transmission, it can be sent in the order optimal for processing
If data is arranged suitably, processing begins as soon as the first data arrives…
YOU DO NOT WAIT FOR THE ENTIRE DATA TO ARRIVE BEFORE PROCESSING BEGINS!†
†Bold, red, super-sized and underlined because there are still people in the CMS trigger community who have not understood this and it is important!

## Slide 46: Spatial Pipelining – Why bother?
By ordering the data geometrically, this allows all algorithms to be fully pipelined†, which in FPGAs means that:
  The processing is localised
  Fan-outs reduced
  Routing delays minimised
  Register duplication eliminated
Experience with Virtex-7 FPGAs has shown that this is VITAL in mapping the design into these very large FPGAs
This will only get more important as devices get larger in future
†That is, pipelined at the full data rate, not at the bunch-crossing rate

## Slide 47: Spatial Pipelining – Why bother?
Full Spatial-Pipelining also allows MAXIMAL logic reuse:
  Case-study: Electron isolation via counting clusters in a ring
  Conventional implementation took >120% of resources available in XC7VX690T FPGA per proposed region
  Spatially-pipelined implementation took 1.5% of resources available in XC7VX690T FPGA per TM node
2 orders of magnitude saving if you do it properly

## Slide 48: The Amdahl-Slotnick debate, 1967
“The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue, this is a decided disadvantage”
Daniel Slotnick, 1967

## Slide 49: Spatial Pipelining – What’s the problem?
You have swapped a spatial axis with the time axis
Positive and negative eta become forward and backward in time
In algorithms, data moving forward in time “interacts” with data moving both forwards and backwards in time
But algorithms are sequential in “real” time – essentially a third time axis
Different granularity data sees time pass at different rates (Time? Which Time?)
Physical data is in registers and transfers between registers also happen in real time but registers occupy physical space within the FPGA and relative spatial placement is important…
Is your head hurting yet?
Forget General Relativity – spatially pipelined firmware is where the real fun is to be had

## Slide 50: The CMS trigger – Run 2: The Present

## Slide 51: The CMS trigger – Run 2
MPC
CSC
DT
LB
RPC
Mezzanine
CuOF
μGMT
New SC & fan-out
New SC & fan-out
Sorting/Merging Layer (Optional)
Endcap
Barrel
Overlap
HF
HCAL
ECAL
Calo Trigger
Preprocessors
Calo Trigger
Main Processors
TCC
oSLB
μHTR
μHTR
Demux
μTF Layer
Endcap
Barrel
Overlap
μGT

## Slide 52: The CMS trigger – Run 2: Systems being upgraded
MPC
CSC
DT
LB
RPC
Mezzanine
CuOF
μGMT
New SC & fan-out
New SC & fan-out
Sorting/Merging Layer (Optional)
Endcap
Barrel
Overlap
HF
HCAL
ECAL
Calo Trigger
Preprocessors
Calo Trigger
Main Processors
TCC
oSLB
μHTR
μHTR
Demux
μTF Layer
Endcap
Barrel
Overlap
μGT

## Slide 53: The CMS trigger – Run 2: Hardware platforms
MPC
CSC
DT
LB
RPC
Mezzanine
CuOF
μGMT
New SC & fan-out
New SC & fan-out
Sorting/Merging Layer (Optional)
Endcap
Barrel
Overlap
HF
HCAL
ECAL
Calo Trigger
Preprocessors
Calo Trigger
Main Processors
TCC
oSLB
μHTR
μHTR
Demux
μTF Layer
Endcap
Barrel
Overlap
μGT

## Slide 54: The CMS trigger – Run 2: Architecture
MPC
CSC
DT
LB
RPC
Mezzanine
CuOF
μGMT
New SC & fan-out
New SC & fan-out
Sorting/Merging Layer (Optional)
Endcap
Barrel
Overlap
HF
HCAL
ECAL
Calo Trigger
Preprocessors
Calo Trigger
Main Processors
TCC
oSLB
μHTR
μHTR
Demux
μTF Layer
Endcap
Barrel
Overlap
Time-Multiplexed
Conventional
μGT
Conventional

## Slide 55: The CMS trigger – Run 2: Hardware platforms
MPC
CSC
DT
LB
RPC
Mezzanine
CuOF
μGMT
New SC & fan-out
New SC & fan-out
Sorting/Merging Layer (Optional)
Endcap
Barrel
Overlap
HF
HCAL
ECAL
Calo Trigger
Preprocessors
Calo Trigger
Main Processors
TCC
oSLB
μHTR
μHTR
Demux
μTF Layer
Endcap
Barrel
Overlap
μGT

## Slide 56: The Master-Processor, Virtex-7 (MP7)
uTCA form factor
72Tx+72Rx 13Gbps optical links
0.9 + 0.9Tb/s signal processor
Xilinx Virtex-7 FPGA
GbE, AMC13/TTC/TTS, PCIe, SAS, SATA, SRIO
On-board firmware repository
Pin-compatible FPGAs allow cost-performance balance
2×144Mbit 550MHz QDR RAM (optional)

## Slide 57: “Base Firmware” Concept

## Slide 58: Floorplan of FPGA

## Slide 59: Floorplan of FPGA
Communication
DAQ
(work in progress)
MGTs and DAQ buffers
MGTs and DAQ buffers
Algorithms
Total LUT usage: 46%
240 MHz clock

## Slide 60: Lessons learned
Floor-planning
  Huge impact on algorithm design
  Structure the algorithm to map optimally onto the FPGA
  Reduces risk that after many hours of routing 6 million nets just 1 or 2 fail to meet timing - exceedingly annoying
  Significant timing improvement
  Only viable if signals remain relatively local
Full pipelining of algorithms is essential - even relatively innocuous looking fan-outs in chips this large have the potential to kill off the entire design
If you want the most out of your FPGA you really need to think creatively about how you structure your data

## Slide 61: The CMS trigger – Run 2: Reality

## Slide 62: The CMS trigger – Run 3: The Future

## Slide 63: The HL-LHC
LHC Run-2
L = O(1034) cm-2s-1
O(10) interactions/bx

## Slide 64: The HL-LHC
LHC Run-2
L = O(1034) cm-2s-1
O(10) interactions/bx
LHC Run-3
L = O(1035) cm-2s-1
O(100) interactions/bx

## Slide 65: The CMS detector
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~83k PbWO4 Ecal Crystals
≡ 40 TBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
Upgrades relevant to triggering
Tracking included in trigger
Full granularity Ecal included in trigger
Complete replacement of endcap Ecal & Hcal

## Slide 66: Big Data: Full granularity Ecal
1 Gb/s
1 Tb/s
1 Pb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
Full Granularity Ecal
61,200 crystals @ 1.6Gb/s = 97.92Tb/s = 386 EB/yr

## Slide 67: Full granularity Ecal: Algorithms
Data is still laid out on a 2D rectilinear grid
Essentially the same as what we do now, only with 5 times the resolution in each direction
Currently, the major question which needs answering is what do the physicists want to do with the extra resolution!

## Slide 68: Big Data: Tracking trigger
1 Gb/s
1 Tb/s
1 Pb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
Tracking Trigger
15,000 modules @ 5Gb/s = 75Tb/s = 296 EB/yr

## Slide 69: Tracking trigger: Algorithms
Track-finding in a high-occupancy environment is HARD
A lot of fake coincidences, noise, overlaps…
Inside solenoid – 4T magnetic field means highly curved tracks
Hough transform
Road search
Projective Iteration
Other?!
?

## Slide 70: Big Data: High-granularity endcap calorimeters (one option)
1 Gb/s
1 Tb/s
1 Pb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
HGcal
30,000 modules @ 10Gb/s = 300Tb/s = 1.2 ZB/yr

## Slide 71: High-granularity endcap calorimeters : Algorithms
Million dollar question!

## Slide 72: Big Data: Tech buzz-word of the moment
1 Gb/s
1 Tb/s
1 Pb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
Run-3 L1T Input
8 seconds of data for the CMS Level-1 trigger in Run-1
0.2 seconds of data for the CMS Level-1 trigger in Run-3

## Slide 73: How to approach the problem

## Slide 74: How to approach the problem
All new systems will use the GBT link
All sending data at the same order of magnitude
It would be sensible for all systems to use a common back-end to receive the data

## Slide 75: How to approach the problem
All new systems will use the GBT link
All sending data at the same order of magnitude
It would be sensible for all systems to use a common back-end to receive the data
We have a system architecture which is scalable to rise to the challenge
We have a system architecture which simplifies boundary handling and is agnostic to the data content
It would be sensible for all systems to use a common trigger platform and common trigger architecture to process the data

## Slide 76: The problems needing solving
To overcome the hardware-centric mindset
Requires a model of collaborative firmware development which is as simple (and rigorous) as collaborative software development

## Slide 77: The problems needing solving
To overcome the hardware-centric mindset
Requires a model of collaborative firmware development which is as simple (and rigorous) as collaborative software development
To overcome the old organizational model

## Slide 78: The problems needing solving
To overcome the hardware-centric mindset
Requires a model of collaborative firmware development which is as simple (and rigorous) as collaborative software development
To overcome the old organizational model
That task could make processing 0.5Pb/s look easy

## Slide 79: The problems needing solving
To overcome the hardware-centric mindset
Requires a model of collaborative firmware development which is as simple (and rigorous) as collaborative software development
To overcome the old organizational model
That task could make processing 0.5Pb/s look easy
Thank you