## Slide 1: Development and testing of an upgrade to the CMS Level-1 Calorimeter Trigger
Andrew W. Rose
Imperial College, London
On behalf of the CMS L1 Calorimeter Trigger upgrade community

## Slide 2: Content
Introduction: The CMS Level-1 Calorimeter Trigger Upgrade
Hardware for upgrades
Hardware testing
System architecture and Firmware
Other work
Conclusions

## Slide 3: Introduction

## Slide 4: The CMS Level-1 Calorimeter Trigger
Mitigate risk by building upgrade in parallel
Stage 1 - improve processing of existing RCT
  New card converts current system to optical
  New HF optical data available
Stage 2 - all inputs in optical format
Current system, albeit modified, operational in parallel
ECAL
energy
HCAL
energy
HF
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
e/γ
Jets

## Slide 5: Stage-1
  oRM
  oSLB
  oRSC
ECAL
energy
HCAL
energy
HF
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
Calorimeter Trigger
Layer 1
Calorimeter Trigger
Layer 2
e/γ
Jets

## Slide 6: Stage-2
  oRM
  oSLB
  oRSC
Eventually decommissioned
ECAL
energy
HCAL
energy
HF
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
Calorimeter Trigger
Layer 1
Calorimeter Trigger
Layer 2
HCAL
energy
e/γ
Jets

## Slide 7: Hardware for upgrades

## Slide 8: Stage-1: oSLB and oRM
ECAL
energy
HCAL
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
HF
energy
oSLB
oRM

## Slide 9: Stage-1: oSLB and oRM
Kintex-7 FPGAs
Mount on existing VME cards, replacing copper links
Testing on-going
  oSLB output looks good
  Working to improve clock stability in oRM
  Latest board-board tests are encouraging
oSLB @ 4.8Gb/s
oSLB
oRM

## Slide 10: Stage-1: oRSC
ECAL
energy
HCAL
energy
Regional Calorimeter Trigger
Global Calorimeter
Trigger
HF
energy

## Slide 11: Stage-1: oRSC
Kintex-7 FPGA
VME interface card
Fits in current RCT crates
18 cards in total
Provides RCT output in optical format to:
  Existing GCT Leaf cards
  Upgrade Layer-2 cards
Microblaze core running Xilinx PetaLinux for service tasks
ECL
to
LVTTL translators
RCT
Clock Interface (NECL)
Avago MiniPOD
Tx Modules
Spartan-6
VME Interface
Kintex-7
XC7K355T
FPGA

## Slide 12: Stage-1: oRSC status
ECL clocks tested – all ok
Reference clocks are fully programmable
  Wide range of synchronous and asynchronous link speeds
Next task – test parallel interface from RCT
  Considered low risk as similar to previous, non-optical, test board
Expect board to be fully validated during the fall & ready for production run thereafter.
ECL
to
LVTTL translators
RCT
Clock Interface (NECL)
Avago MiniPOD
Tx Modules
Spartan-6
VME Interface
Kintex-7
XC7K355T
FPGA

## Slide 13: Stage-2
ECAL
energy
HF
energy
Calorimeter Trigger
Layer 1
Calorimeter Trigger
Layer 2
HCAL
energy
University of Wisconsin
CTP7

## Slide 14: Stage-2: CTP7
Based on Virtex-7 XC7VX690T FPGA
Zynq processor running Xilinx PetaLinux for service tasks
Baseline Layer 1 hardware
Link power distribution to support a mixture of speeds
  4.8/6.4 Gbps inputs
  9.6/10 Gbps outputs
Schematic design completed
Layout in progress
Component count will be:
  Higher than CTP6 (μTCA)
  Lower than oRSC (VME)
CTP6 – Virtex-6 based prototype for CTP7
See TWEPP 2012:
https://indico.cern.ch/contributionDisplay.py?contribId=86&confId=170595&sessionId=51
https://indico.cern.ch/contributionDisplay.py?contribId=97&confId=170595&sessionId=53
CTP6

## Slide 15: Stage-2:
1.5Tb/s optical signal processor
Xilinx Virtex-7 FPGA:
  XC7VX485T or XC7VX690T
Advanced boot-loader & diagnostics (full system test at start-up)
On-board firmware repository
2×144Mbit 550MHz QDR RAM (optional)
Been in hand for over a year
  Continuous testing over that period
  Very well understood
Extensive software and firmware
Imperial MP7 processor board
See also TWEPP 2012:
https://indico.cern.ch/contributionDisplay.py?contribId=86&confId=170595&sessionId=51
https://indico.cern.ch/contributionDisplay.py?contribId=97&confId=170595&sessionId=53

## Slide 16: Hardware testing

## Slide 17: Optical/serial link validation
These boards:
  Have a lot of serial links
  Run these links fast
  Use new form-factor MiniPOD optics
Stringent testing must be board-to-board, not loopback
Scaling effects must be considered
  Number of links
  Line rate
Cross-generational differences
  Transceivers in 7-series FPGAs behave very differently to 5- or 6- series devices
72 @ 10Gb/s → 62.2Pb/day → ~1Eb every 2 weeks
No bit errors

## Slide 18: Optical link validation
MP7 optical links worked perfectly out-of-the-box
  MiniPODs are using default pre-emphasis (minimal)
  TX differential swing is minimal
  No pre-emphasis/de-emphasis in MGTs
oRSC also has working optical links
Optical eye
@ 10Gb/s
Optical eye
@ 6.4Gb/s
oRSC

## Slide 19: Serial link validation
New feature in Xilinx 7-series is the ability to generate eye-diagrams inside the transceivers themselves
Extensively tested all 72 links running PRBS7 at 10Gb/s, LPM
Various line rates validated, including LHC-synchronous operation
  Eye-diagrams for all line-rates meet industry standards
XC7VX485T – GTX transceivers
XC7VX690T – GTH transceivers
1Gb/s
2Gb/s
4Gb/s
5Gb/s
8Gb/s
10Gb/s
1Gb/s
2Gb/s
4Gb/s
5Gb/s
8Gb/s
10Gb/s
MGT configuration done at runtime, not build-time, giving significantly greater flexibility and control
O(1016) bits per link transferred without bit error

## Slide 20: Integration testing
Homogeneous hardware is easier to test than heterogeneous hardware
Unfortunately CMS trigger hardware is not homogeneous
Integration facility set up at CERN for testing
Testing with deployment infrastructure:
  Trigger, Timing and Control (TTC)
  Computing, networks, etc.
Internal progress monitoring milestones:
  Last, in July
  Next, next week
RCT
oRSC
GCT
oSLB
oRM
Layer 2
(MP7)
Layer 1
(CTP7)
µHTR
CTP6

## Slide 21: Integration testing
oRSC
Optical patch panel for oRSC
Optical patch panel for MP7
CTP6
Real life is never so neat and tidy

## Slide 22: Integration testing: July
July integration test was first scheduled integration test
Focussed on link quality between boards
Follow-up test being scheduled for those tasks not completed in July
Link | Oscilloscope | IBERT | Data patterns | Alignment
oSLB – oRM |  |  |  | 
uHTR – oRM |  |  |  | 
oRM – RCT |  | – |  | 
uHTR – CTP6 |  |  |  | 
oSLB – CTP6 |  |  |  | 
RCT – oRSC |  | – |  | 
oRSC – CTP6 |  |  |  | 
oRSC – MP7 |  |  |  | 
oRSC – GCT |  |  |  | 
CTP6 – CTP6 |  |  |  | 
MP7 – MP7 |  |  |  | 

## Slide 23: System architecture and firmware

## Slide 24: Algorithm firmware
Rutherford Appleton Laboratory
Generic processing boards with single I/O format converts trigger development from a hardware problem to a programming problem
Allows collaborative development of algorithms
Iceberg Technology

## Slide 25: Time-multiplexed trigger
Layer 1
“Preprocessors”
Layer 2
“Processing nodes”
The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue this is a decided disadvantage. Daniel Slotnick, 1967

## Slide 26: Algorithm firmware
The Time-multiplexed architecture allows all data arrives in geometric order:
  Towers at given φ are always the same bits on the same optical links
  Towers arrive in order of increasing |η|
This converts a 2D geometric problem to a 1D problem
This allows all algorithms to be fully pipelined:
  The processing is localised
  Fan-outs reduced
  Routing delays minimised
  Register duplication eliminated
Engineers and computer-scientists have long reported that full-pipelining is the preferred design methodology for FPGAs

## Slide 27: Algorithm firmware
Time-multiplexed trigger has been demonstrated:
  Using existing GCT algorithms on Mini-T5 card
  Using baseline upgrade algorithms on Mini-T5 card
  Using existing GCT algorithms on MP7 card
September integration test is a test of:
  Dataflow from level-1 to level-2 at 10Gbps
  Baseline upgrade algorithms in the final processing hardware
  Infrastructure, such as computing and TTC
Links
Towers
Partial
Clusters
Ring Segments
Strips
Ring Sums
Clusters
Jets (6 types)
e/γ/τ Classifiers
Sort
Overlap Filter
Algorithms available for integration test
Mini-T5 TMT demonstrator Sept 2011
Rutherford Appleton Laboratory
Iceberg Technology

## Slide 28: 7-series Firmware
Large 7-series FPGAs are beasts!
Scale of routing problem has outstripped performance of PCs
Xilinx has invested heavily in improving tools
Still have to work a lot harder at optimising designs than we used to
Rutherford Appleton Laboratory
Iceberg Technology
Conceptual layout of algorithms from the upgrade TDR
Bandwidth
Logic

## Slide 29: 7-series Firmware
Large 7-series FPGAs are beasts!
Image shows Calo trigger main processor
  72 input links @ 10 Gbps
  250MHz deserialized operation
Build-time: 4-6 hours
  Much better than the >24hours reported elsewhere!
Extensive use of floor-planning tools
  Localized (fully-pipelined) logic makes this a lot easier
Rutherford Appleton Laboratory
Iceberg Technology

## Slide 30: 7-series Firmware
Large 7-series FPGAs are beasts!
Image shows Calo trigger main processor
  72 input links @ 10 Gbps
  250MHz deserialized operation
Build-time: 4-6 hours
  Much better than the >24hours reported elsewhere!
Extensive use of floor-planning tools
  Localized (fully-pipelined) logic makes this a lot easier
Rutherford Appleton Laboratory
Iceberg Technology

## Slide 31: Other work

## Slide 32: Other work
UW/Desy IPMI system manager
A standardized HAL for µTCA adopted
GUI tools under development
Python bindings
Imperial/Bristol/ RAL/CERN
UW have been experimenting with embedded Linux in soft and hard core FPGAs
MP7-XE - optimised for 13Gb/s links
Plus lots more that didn’t have any pretty pictures

## Slide 33: Conclusions

## Slide 34: Conclusions
A lot of progress made in the last year!
Hardware in hand
  MP7 has been being validated for over a year
  oSLB, oRM and oRSC now available and testing on-going
Baseline upgrade architecture and hardware now decided upon
  Time-multiplexed Trigger
  CTP7 at layer-1
  MP7 at layer-2
Can now look more towards systems-level integration
A lot still to do…

## Slide 35: Spares

## Slide 36: Imperial College London University of Bristol RAL

## Slide 37: Time-multiplexed trigger
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
3
3
3
3
3
3
3
3
3
3
3
3
3
3
3
3
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
All data for 1bx from all regions in a single card!
Everything you need!
5
5
5
5
5
5
5
5
5
5
5
5
5
5
5
5
1
2
6
6
6
6
6
6
6
6
6
6
6
6
6
6
6
6
7
7
7
7
7
7
7
7
7
7
7
7
7
7
7
7
All data for 1bx from all regions in a single card!
Everything you need!
All data for 1bx from all regions in a single card!
Everything you need!
BX:1
BX:2
BX:3
BX:4
BX:5
BX:6
BX:7

## Slide 38: Automated Link alignment firmware
Fixed, low Latency GTX/GTH Serdes Link
Asynchronous or Synchronous with LHC clock
Rx buffer bypassed for low latency & asynchronous clock capability
CRC32 integrity checks
Locks to TTC timing
Spy buffer
Only 256 orbits to align
the entire system
Has been in continuous
use in hardware for over
a month

## Slide 39: Other tests
All the auxiliary subsystems on the MP7 have also been validated:
Mezzanine I/O
QDR-II+ RAM
Board communication (Ethernet)
USB 2.0 OTG, IPMI, SD card repository (microcontroller)
SPI PROM (protected bootloader)
Thermal dissipation, humidity & temperature monitoring
Power consumption, phasing & monitoring
I/O fan-out mezzanine for debugging
30 differential pairs to/from the FPGA
3v3, 2v5 and 1v8 supplies
Dedicated I2C lines to the microcontroller

## Slide 40: On-board Firmware Repository
The MMC on the MP7 also acts as controller of the on-board firmware repository
Loading firmware into the FPGA from the SD-card takes ~3s cf. ~2s using the flash PROM – i.e. no noticeable penalty.
The time taken to write new firmware to the card over IPbus will be measured when the MMC-FPGA IPbus interface is completed (end of month). Should be of the order 1 to 10’s of seconds instead of many minutes for NOR flash.
On-board repository means that once a firmware is written to the board, it need never be written to the board again (roll-back is a change of configuration key)
Because it is SD card based, for new boards the repository can be written directly to the SD card from a PC (this is how the uSD card is used currently)

## Slide 41: Firmware Implementation status
Rutherford Appleton Laboratory
Iceberg Technology

## Slide 42: Website
www.hep.ph.ic.ac.uk/mp7

## Slide 43: University of Wisconsin

## Slide 44: oRSC to CTP6 Integration Test
Performed at CMS integration facility. As close as possible to final operating conditions
Bit error rate < 10-14

## Slide 45: oRSC to CTP6 Integration Test
Data patterns successful transmitted from the oRSC, captured on the CTP6, and readout via embedded Linux
Fibre Capture RAM readout
SW controllable capture
Capture RAM auto clears on each capture
All six links capture expected pattern from oRSC
Capture automatically checked by host
Patterns being successfully captured
Data flow in integration test

## Slide 46: Microblaze and PetaLinux
Microblaze is soft-processor Xilinx IP core
PetaLinux is a proprietary embedded Linux product owned by Xilinx
Runs on the Microblaze and ZYNQ platforms
Comes with standard drivers for GigE, I2C, SPI, USART, Flash, etc.
Housekeeping functionality can now be written by software inclined people as Linux or embedded C applications
Board | Control FPGA | Workhorse FPGA
oRSC | Microblaze | Microblaze
CTP6 | Microblaze | Microblaze
CTP7 | ZYNQ | Microblaze

## Slide 47: Embedded Processor Concept
Embedded processor moves service tasks from Firmware to Software
  Shortens design cycle
  Remove FPGA design and integration burden for commodity interface cores
  Utilize embedded system IP
  Interfaces more flexible under software control
  Conform to industry standards at core
  Add software application above core to specialize
Ensures FPGA design focus on custom logic
  Custom high speed communication interfaces
  Custom physics algorithms

## Slide 48: CTP7 Zynq SoC Linux Control Chip
ZYNQ has hard ARM core
Embedded Linux on chip transforms housekeeping tasks into Linux application
Xilinx AXI chip-to-chip exposes Target FPGA into ZYNQ memory space
Target AMC Board
SDRAM
Low Speed Peripherals (EEPROM, Clock Synths, Optical Modules, Crosspoint Switches, Console, etc.)
Target
FPGA
AXI
Chip-to-Chip
Interface
SPI Config Interface
GbE Connection
ZYNQ
SoC
(Linux)
microSD
Flash
Memory

## Slide 49: IPMI System Manger
μTCA features Gigabit Ethernet to address individual slots and IPMI to manage the power and sensors of individual cards
Commercial IPMI management tools available, but
  Vendor specific
  Not extensible (GUIs)

## Slide 50: IPMI System Manger
API wrapping a socket interface
Act as a gateway for other applications into the IPMI system
Provide a robust IPMI-over-LAN connection to crates
Provide a service for automatic low-level initialization of AMC cards at start-up
GUI using System Manger API
Developed at DESY
Crate MCH