## Slide 1: Experience powering Virtex-7 FPGAs
Andrew W. Rose, Gregory M. Iles
Imperial College, London

## Slide 2
1.5Tb/s optical signal processor
Xilinx Virtex-7 FPGA:
  XC7VX485T or XC7VX690T
Advanced boot-loader & diagnostics (full system test at start-up)
On-board firmware repository
2×144Mbit 550MHz QDR RAM (optional)
Been in hand for over a year
  Continuous testing over that period
  Exceptionally well understood
Imperial MP7 processor board
See also TWEPP 2012: https://indico.cern.ch/contributionDisplay.py?contribId=86&confId=170595&sessionId=51
https://indico.cern.ch/contributionDisplay.py?contribId=97&confId=170595&sessionId=53

## Slide 3: FPGA architecture
MP7 uses XC7VX485T or XC7VX690T
Pin-compatible FFG1927 package
This is how the XC7VX690T looks in the documentation:

## Slide 4: FPGA architecture
MP7 uses XC7VX485T or XC7VX690T
Pin-compatible FFG1927 package
And if we colour in the power pins:
Half of the pins on the chip are dedicated to powering the thing

## Slide 5: MP7 board – Top half
Transmitters
Transmitters
Receivers
Receivers
FPGA
2v5
3v3
1v0
1v5
1v8
Header

## Slide 6: MP7 board – Bottom half
A1v0
A1v2
QDR
QDR
CPLD
μC
Clk
USB
μSD
Clocking
2v5
3v3
1v0
1v5
1v8
A1v0
A1v2
A1v8
A1v8

## Slide 7: MP7 R0 power architecture
Bulk regulators
Speciality and secondary regulators

## Slide 8: MGTs
MP7 is an optical stream processor
72 links @ >10Gb/s, fully bidirectional
7-series MGTs require:
  1v0
  1v2
  1v8
but there are very tight constraints!
MGTs
MGTs

## Slide 9: MGTs
The noise limits and tolerances on the MGT power supplies are tight!
There are also constraints on voltage drop across the chip
  Ohmic losses in the planes required that the regulators are as close as possible to the MGTs
  There are two banks of MGTs
  Each needed powering independently
Space constraints also mean that the 10Gb/s signals run underneath the regulators
Noise was a concern…

## Slide 10: MGTs: Revision 0
Favoured LTM4606 6A ultralow-EMI switch-mode regulators by Linear, since:
  These are designed for transceiver applications
  Are sufficiently low that the fitted on the bottom of the board
  We had used these successfully on the Mini-T5 card
Included a regulator on a test board to test for interference
Also, taped a Samtec kapton cable to top of regulator and tested 10Gb/s signal integrity that way
Good news – regulator had no effect on a 10G signal passing under it

## Slide 11: MGTs: Revision 0
Card was designed before 7-series engineering silicon was available
LTM4606 should have had ~35% headroom based on Xilinx’s power estimator
When card assembled and tested, power consumption 30% to 220% higher than Xilinx had predicted
A lot of discussion with Xilinx engineers – found a lot of “features” that Xilinx weren’t aware of. The price you pay for living at the cutting edge.
Greg Iles made a huge number of measurements

## Slide 12: MGTs: Revision 0
Very impressed with LTM4606
  Rated 6A nominal
  8A peak
But performed excellently even when run flat-out at 25% above its nominal rating

## Slide 13: MGTs: Revision 1
We were very concerned about the possibility of power supply changes introducing noise
Several test cards were made to test alternative power supply designs on an R0 card
Noise was measured both electrically and by its effect on the error-rate of the 10Gb/s optical links
LTM4601 switch-mode regulator by Linear won the day:
  Same size as the LTM4606 (although different footprint)
  Similar external components
  Simple replacement
LTM4601 after ferrite

## Slide 14: MGTs: Revision 1
  485, RPBS7, 10G, QPLL, 24 links (one side),
  Plots show bathtub from 6 different links: 1 from each quad
Magnus Loutit
Statistical Floor
Statistical Floor
New PSU
Original PSU

## Slide 15: Core power
Large BGAs puncture the board with vast forest of vias
  Increase the effective resistivity of the power planes
Core power pins are at centre of BGA
Use fills in three layers to get power into core to ensure sufficient current
  Prefer layers with 1oz copper over ½oz copper layers
Use remote sense, even though the distance is only a few cm

## Slide 16: Power supply monitoring
MP7 makes extensive use of LTC2990 four channel voltage/current/power and temperature monitor
  Sub-millivolt resolution
  1% current resolution
  1% temperature resolution
  10-Lead MSOP Package – size is important in the space-constrained µTCA environment
MP7 measures:
  Both incoming supplies
  ALL bulk supplies on the board
  Subset of secondary/speciality supplies
Sensors are distributed around the board allowing an approximate temperature profile of the board

## Slide 17: Power consumption sensitivity
Power consumed by the Virtex-7 can be extraordinarily sensitive to configuration flags
Unused and non-optimally configured resources can contribute massively to power consumption. Not always immediately obvious.
Need to consider the entire design (all configuration flags) before making statements about power consumption
No substitute for hands-on experience

## Slide 18: With great power come great heat dissipation…
With early revision of board, 48-link design hit thermal cut-out when on the bench (no fans). Reached 60°C in a crate.
Designed a heatsink ourselves (old-school educated guesswork, no simulations) and prototyped in-house. Dissipated 40% more power than the off-the shelf part. Temperature didn’t exceed 45°C in 48-link design.
Production heatsinks manufactured externally and anodized (increase radiative transfer by further 25%)
First attempt: Off the shelf
Final version: Designed in-house

## Slide 19: Conclusions
The compact nature and excellent performance of Linear’s switch-mode modules make them an excellent match for 7-series FPGAs and the µTCA environment, where space is constrained
Xilinx power estimator should be considered exactly that… AN ESTIMATOR
  Don’t rely on it being correct
  It is no substitute for hands-on experience
7-series FPGAs have a large number of configuration flags and it is not always immediately obvious how these will affect power consumption