## Slide 1: Fully Parallel Architectures: FPGAs, Pipelining and Systolic arrays
Andrew W. Rose
Image credit to Sophia Shao @ UC Berkley & Vivienne Sze @ MIT

## Slide 2: Before we start…
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 3: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 4: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
That would just be stupid

## Slide 5: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
That would just be stupid
But this is essentially what a CPU does

## Slide 6: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 7: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
So why doesn’t my PC do this?

## Slide 8: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
Because writing code like this is *really, really* hard
So why doesn’t my PC do this?

## Slide 9: Recap: Field Programmable Gate Arrays (FPGAs)
2D array of Programmable Logic Blocks
Massive Fabric of Programmable Interconnects

## Slide 10: Programmable Interconnect matrix

## Slide 11: Combinatorial Logic Block
SRAM based look-up table to transform any input to any compile-time defined output

## Slide 12: One way to use an FPGA
Wait for the signal to propagate
“Sea-of-logic” approach
Data In
Data Out

## Slide 13: One way to use an FPGA
Wait for the signal to propagate
“Sea-of-logic” approach
Constrained by the speed of light
Data In
Data Out

## Slide 14: Better…
Wait for the signal to propagate
“Sea-of-logic” approach
Constrained by the speed of light
Do less
Clock the result
Data In
Data Out
Data In

## Slide 15: Better…
Wait for the signal to propagate
“Sea-of-logic” approach
Constrained by the speed of light
Do less
Clock the result
Data In
Data Out
Data In

## Slide 16: Better…
Wait for the signal to propagate
“Sea-of-logic” approach
Constrained by the speed of light
Do less
Clock the result
Data In
Data Out
Data In

## Slide 17: Better…
Wait for the signal to propagate
“Sea-of-logic” approach
Constrained by the speed of light
Do less
Clock the result
Data In
Data Out
Data In

## Slide 18: Better…
Wait for the signal to propagate
“Sea-of-logic” approach
Constrained by the speed of light
Do less
Clock the result
Data In
Data Out
Data In

## Slide 19: Better…
Wait for the signal to propagate
“Sea-of-logic” approach
Constrained by the speed of light
Do less
Clock the result
Doing less on each clock but compensated for by much higher clock speeds
Data In
Data Out
Data In
Data Out

## Slide 20: Breaking down algorithms like this is HARD
“The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue, this is a decided disadvantage”
Daniel Slotnick, 1967
It's all about data-structure
  It's all about data-structure
    It's all about data-structure
      It's all about data-structure
        It's all about data-structure
          It's all about data-structure
            It's all about data-structure

## Slide 21: But…
Accepting new data on every clock cycle is one extreme
  Fully pipelined
  "Full FPGA"

## Slide 22: But…
Accepting new data on every clock cycle is one extreme
  Fully pipelined
  "Full FPGA"
Each block can accept new data less frequently than every clock cycle
  Called the Interval

## Slide 23: But…
Accepting new data on every clock cycle is one extreme
  Fully pipelined
  "Full FPGA"
Each block can accept new data less frequently than every clock cycle
  Called the Interval
Each block can (but doesn't have to) emit data at a different rate to the input
  Think of an accumulator receiving data every clock, and emitting and resetting the sum on every 10th clock cycle

## Slide 24: But…
Accepting new data on every clock cycle is one extreme
  Fully pipelined
  "Full FPGA"
Each block can accept new data less frequently than every clock cycle
  Called the Interval
Each block can (but doesn't have to) emit data at a different rate to the input
  Think of an accumulator receiving data every clock, and emitting and resetting the sum on every 10th clock cycle
  Or receiving data every 10th clock, and applying and outputting 10 different operations to that data

## Slide 25: But…
Accepting new data on every clock cycle is one extreme
  Fully pipelined
  "Full FPGA"
Each block can accept new data less frequently than every clock cycle
  Called the Interval
Each block can (but doesn't have to) emit data at a different rate to the input
  Think of an accumulator receiving data every clock, and emitting and resetting the sum on every 10th clock cycle
  Or receiving data every 10th clock, and applying and outputting 10 different operations to that data
We can still use the ideas of pipelining and 2D arrays
  Referred to generically as Systolic arrays

## Slide 26: Start simple: How do we add a lot of numbers?

## Slide 27: Start simple: How do we add a lot of numbers?
The English say:
There's more than one way to skin a cat

## Slide 28: Start simple: How do we add a lot of numbers?
Summation chain
+
Input
Output
+
Input
+
Input
+
Input
+
Input
+
Input
+
Input
+
Input
+
Input
+
Input

## Slide 29: Start simple: How do we add a lot of numbers?
Accumulator
+
Input
Output

## Slide 30: Start simple: How do we add a lot of numbers?
Tree adder
+
+
Input
Input
Input
Input
+
+
+
Input
Input
Input
Input
+
+
Output

## Slide 31: Start simple: How do we add a lot of numbers?
Which is the best approach?

## Slide 32: Start simple: How do we add a lot of numbers?
Which is the best approach?
  Depends on your scenario

## Slide 33: Start simple: How do we add a lot of numbers?
Which is the best approach?
  Depends on your scenario
And there is no reason why you can't mix-and-match

## Slide 34: Start simple: How do we add a lot of numbers?
“The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue, this is a decided disadvantage”
Daniel Slotnick, 1967
Which is the best approach?
  Depends on your scenario
And there is no reason why you can't mix-and-match

## Slide 35: Recall
Accessing DRAM is EXPENSIVE
Accessing DRAM is SLOW

## Slide 36: Recall: Memory Access is the Bottleneck
Worst Case: all memory R/W are DRAM accesses
Example: AlexNet [NIPS 2012] has 724M MACs vs. 2896M DRAM accesses required
Weights
Inputs
Partial Sum
Updated partial Sum

## Slide 37: Recall: Leverage Local Memory for Data Reuse
Allows elements to be reused
  Temporal Reuse
Extra levels of local memory hierarchy
Smaller, but Faster and more Energy-Efficient

## Slide 38: Recall: Data Reuse in DNN
Convolutional Reuse
(Conv layers only)
Reuse: Inputs
Weights
Input Reuse
(Conv and fully-connected layers) Reuse: Inputs
Filter Reuse
(Conv and fully-connected layers, batch size > 1) Reuse: Weights
Filter
Input
Filter
Input
Filter
Input

## Slide 39: Recall: Data Reuse in DNN
Convolutional Reuse
(Conv layers only)
Reuse: Inputs
Weights
Input Reuse
(Conv and fully-connected layers) Reuse: Inputs
Filter Reuse
(Conv and fully-connected layers, batch size > 1) Reuse: Weights
If all data reuse is exploited, DRAM accesses in AlexNet can be reduced from 2896M to 61M (best case)
Filter
Input
Filter
Input
Filter
Input

## Slide 40: Single PE for GEMM (and by extension any NN)
Input Activation
Weight
Output Activation
Register
Register
Register
MAC
ALU
or
Processing element

## Slide 41: Example: 1D convolution
Output Stationary (OS)
for( q=0; q<Q; q++ ){ for( s=0; s<S; s++ ){ O[q] += I[q+s] * W[s]; } }
Output
Weight
Input
×U
×S
×Q

## Slide 42: Output Stationary: Temporal reuse
for( q=0; q<Q; q++ ){ for( s=0; s<S; s++ ){ O[q] += I[q+s] * W[s]; } }
Output
Weight
Input
×U
×S
×Q

## Slide 43: Output Stationary: Temporal reuse
for( q=0; q<Q; q++ ){ for( s=0; s<S; s++ ){ O[q] += I[q+s] * W[s]; } }
Output
Weight
Input
×U
×S
×Q
Each output used repeatedly

## Slide 44: Output Stationary
The naïve way to implement it in our Processing Element
Input Activation from Cache
Weight from Cache
Output Activation to/from Cache
MAC
ALU
or
Processing element

## Slide 45: Output Stationary
And only one RAM write required at the end of the accumulation
Input Activation from Cache
Weight from Cache
Output Activation to Cache
Register
MAC
ALU
or
Processing element

## Slide 46: Example: 1D convolution
for( q=0; q<Q; q++ ){ for( s=0; s<S; s++ ){ O[q] += I[q+s] * W[s]; } }
for( s=0; s<S; s++ ){ for( q=0; q<Q; q++ ){ O[q] += I[q+s] * W[s]; } }
Output
Weight
Input
×U
×S
×Q
Output Stationary (OS)

## Slide 47: Example: 1D convolution
Output Stationary (OS)
for( q=0; q<Q; q++ ){ for( s=0; s<S; s++ ){ O[q] += I[q+s] * W[s]; } }
Weight Stationary (WS)
for( s=0; s<S; s++ ){ for( q=0; q<Q; q++ ){ O[q] += I[q+s] * W[s]; } }
Output
Weight
Input
×U
×S
×Q

## Slide 48: Weight Stationary: Temporal reuse
for( s=0; s<S; s++ ){ for( q=0; q<Q; q++ ){ O[q] += I[q+s] * W[s]; } }
Output
Weight
Input
×T
×S
×Q
Each weight used repeatedly

## Slide 49: Weight Stationary
Input Activation from Cache
Weight from Cache
Output Activation to/from Cache
Register
MAC
ALU
or
Processing element

## Slide 50: Of course, a third option: Input Stationary
for( q=0; q<Q; q++ ){ for( s=0; s<S; s++ ){ O[q] += I[q+s] * W[s]; } }
for( u=0; u<U; u++ ){ for( s=0; s<S; s++ ){ O[u-s] += I[u] * W[s]; } }
Input Activation from Cache
Weight from Cache
Output Activation to/from Cache
Register
MAC
ALU
or
Processing element
Output
Weight
Input
×U
×S
×Q
Beware:
u-s >= 0 u-s < Q

## Slide 51: Use parallelism to improve compute performance

## Slide 52: Highly-Parallel Compute Paradigms
Temporal Architecture (SIMD/SIMT)

## Slide 53: Highly-Parallel Compute Paradigms
Temporal Architecture (SIMD/SIMT)
Spatial Architecture (Dataflow Processing)

## Slide 54: So what can you do with dataflow processing?

## Slide 55: Why systolic array processors?
Moving data from one ALU to another in a systolic array is *much, much* cheaper than moving data from DRAM
  Cheaper even than from a local buffer/cache

## Slide 56: Matrix Multiply
for( m=0; m<M; m++ ){ for( n=0; n<N; n++ ){ O[n, m] = 0; for( k=0; k<K; k++ ){ O[n, m] += I[m, k] * W[k, n]; } O[n, m] = Activation( O[n, m] ); } }

## Slide 57: Matrix Multiply
Adder Tree
Typical width: 8-64
Applicable to any accumulation dimensions
E.g. NVDLA, DianNao
for( m=0; m<M; m++ ){ for( n=0; n<N; n++ ){ O[n, m] = 0; spatial_for( k=0; k<K; k++ ){ O[n, m] += I[m, k] * W[k, n]; } O[n, m] = Activation( O[n, m] ); } }
+
+
+
+
+
+
+
Output
×
×
×
×
×
×
×
×

## Slide 58: Matrix Multiply
Adder Tree
Typical width: 8-256
Applicable to any accumulation dimensions
E.g. Google TPU, Gemmini
for( m=0; m<M; m++ ){ for( n=0; n<N; n++ ){ O[n, m] = 0; spatial_for( k=0; k<K; k++ ){ O[n, m] += I[m, k] * W[k, n]; } O[n, m] = Activation( O[n, m] ); } }
+
×
+
×
+
×
+
×
+
×
+
×
+
×
+
×
Output

## Slide 59: Can also use parallelism for Spatial Reuse

## Slide 60: Can also use parallelism for Spatial Reuse
Direct-wiring Multicast
Up against the speed of light

## Slide 61: Can also use parallelism for Spatial Reuse
Systolic Multicast
Registered at each step
Signal can go further
Clocks can run faster

## Slide 62: Slightly more advanced PE
Input Activation
Weight
Output Activation
Register
Register
Register
MAC
Processing element
Partial Sum
Register
Forwarding

## Slide 63: Matrix Multiply
Direct-wiring multicast
Typical width: 16
Applicable to any non-accumulation dimensions
E.g. NVDLA, DianNao
spatial_for( m=0; m<M; m++ ){ for( n=0; n<N; n++ ){ O[n, m] = 0; for( k=0; k<K; k++ ){ O[n, m] += I[m, k] * W[k, n]; } O[n, m] = Activation( O[n, m] ); } }
+
×
+
×
+
×
+
×
+
×
+
×
+
×
+
×

## Slide 64: Matrix Multiply
Systolic multicast
Typical width: 8-256
Applicable to any non-accumulation dimensions
E.g. Google TPU, Gemmini
spatial_for( m=0; m<M; m++ ){ for( n=0; n<N; n++ ){ O[n, m] = 0; for( k=0; k<K; k++ ){ O[n, m] += I[m, k] * W[k, n]; } O[n, m] = Activation( O[n, m] ); } }
+
×
+
×
+
×
+
×
Register
Register
Register

## Slide 65: Put it together: NVDLA
Direct-wiring multicast
Adder Tree
+
+
+
+
+
+
+
Output
×
×
×
×
×
×
×
×
+
+
+
+
+
+
+
Output
×
×
×
×
×
×
×
×
+
+
+
+
+
+
+
Output
×
×
×
×
×
×
×
×
+
+
+
+
+
+
+
Output
×
×
×
×
×
×
×
×
spatial_for( m=0; m<M; m++ ){ for( n=0; n<N; n++ ){ O[n, m] = 0; spatial_for( k=0; k<K; k++ ){ O[n, m] += I[m, k] * W[k, n]; } O[n, m] = Activation( O[n, m] ); } }

## Slide 66: Put it together: Google TPU
Systolic multicast
Systolic accumulation
spatial_for( m=0; m<M; m++ ){ for( n=0; n<N; n++ ){ O[n, m] = 0; spatial_for( k=0; k<K; k++ ){ O[n, m] += I[m, k] * W[k, n]; } O[n, m] = Activation( O[n, m] ); } }
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg
+
×
Reg
Reg

## Slide 67: Put it together: Systolic TPU in action
Inputs
Outputs
Weights
PE
PE
PE
PE

## Slide 68: Put it together: Systolic TPU in action
Preload weights into registers
  Weight Stationary (WS)
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22

## Slide 69: Put it together: Systolic TPU in action
Optimally arrange your input
  It's all about data-structure
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a11
a21
a12
a22

## Slide 70: Put it together: Systolic TPU in action
Clock the systolic array – clock 0
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a11
a21
a12
a22

## Slide 71: Put it together: Systolic TPU in action
Clock the systolic array – clock 0
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a11
a21
a12
a22
a11.b11

## Slide 72: Put it together: Systolic TPU in action
Clock the systolic array – clock 1
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a11
a21
a12
a22
a11.b11

## Slide 73: Put it together: Systolic TPU in action
Clock the systolic array – clock 1
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a11
a21
a12
a22
a11.b11 +a12.b21
a11.b11
a21.b11
a11.b12

## Slide 74: Put it together: Systolic TPU in action
Clock the systolic array – clock 1
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a11
a21
a12
a22
a11.b11
a21.b11
a11.b12
a11.b11 +a12.b21
c11

## Slide 75: Put it together: Systolic TPU in action
Clock the systolic array – clock 2
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a21
a12
a22
a21.b11
a11.b12
a11

## Slide 76: Put it together: Systolic TPU in action
Clock the systolic array – clock 2
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a21
a12
a22
a21.b11
a11.b12
a21.b11 +a22.b21
a21.b12
a11
a11.b12 +a12.b22

## Slide 77: Put it together: Systolic TPU in action
Clock the systolic array – clock 2
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a21
a12
a22
a21.b11
a11.b12
a21.b11 +a22.b21
a21.b12
a11
a11.b12 +a12.b22
c21
c12

## Slide 78: Put it together: Systolic TPU in action
Clock the systolic array – clock 3
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a21
a12
a22
a21.b12

## Slide 79: Put it together: Systolic TPU in action
Clock the systolic array – clock 3
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a21
a12
a22
a21.b12
a21.b12 +a22.b22

## Slide 80: Put it together: Systolic TPU in action
Clock the systolic array – clock 3
Inputs
Outputs
Weights
PE
PE
PE
PE
b11
b12
b21
b22
a21
a12
a22
a21.b12
a21.b12 +a22.b22
c22
Success!

## Slide 81: Summary of dataflow architectures
Minimizing data movement is the key to achieving high energy efficiency for DNN accelerators
Dataflow taxonomy:
  Output Stationary: minimize movement of partial sums
  Weight Stationary: minimize movement of weights
  Input Stationary: minimize movement of inputs
There are many ways to skin a cat
  Which is the best approach? Depends on your scenario
  And there is no reason why you can't mix-and-match approaches

## Slide 82: Summary of dataflow architectures
With sequential-processing your data needs to be in the right place in a 1D memory
With data-flow processing your data needs to be in both the right place in an N-Dimensional space and at the right time
And that is why writing code like this is *really, really hard*