## Slide 1: Quantization, Sparsity and Pruning
Andrew W. Rose
Image credit to Sophia Shao @ UC Berkley & Vivienne Sze @ MIT

## Slide 2: Recall
Accessing DRAM is EXPENSIVE
Accessing DRAM is SLOW

## Slide 3: Scientific Notation (in Decimal)
Normalized form has exactly one, non-zero digit to left of decimal point
1/1,000,000,000 = 1.0 x 10-9 = 0.1 x 10-8 = 10.0 x 10-10 = …
3.14ten × 103210
Exponent
Mantissa
Decimal point
Radix (Base)
ten

## Slide 4: Scientific Notation (in Decimal)
Normalized form has exactly one, non-zero digit to left of decimal point
1/1,000,000,000 = 1.0 x 10-9 = 0.1 x 10-8 = 10.0 x 10-10 = …
3.14ten × 103210
Exponent
Mantissa
Decimal point
Radix (Base)
Normalised
ten

## Slide 5: Scientific Notation (in Decimal)
Normalized form has exactly one, non-zero digit to left of decimal point
1/1,000,000,000 = 1.0 x 10-9 = 0.1 x 10-8 = 10.0 x 10-10 = …
3.14ten × 103210
Exponent
Mantissa
Decimal point
Radix (Base)
Normalised
Denormalised
ten

## Slide 6: Scientific Notation (in Binary)
Normalized form has exactly one, non-zero digit to left of binary point
1.01two × 23210
Exponent
Mantissa
Binary point
Radix (Base)
ten

## Slide 7: Scientific Notation (in Binary)
Normalized form has exactly one, non-zero digit to left of binary point
  But in Binary this is always a 1 – We do not need to store it!
1.01two × 23210
Exponent
Mantissa
Binary point
Radix (Base)
ten

## Slide 8: Scientific Notation (in Binary)
Normalized form has exactly one, non-zero digit to left of binary point
  But in Binary this is always a 1 – We do not need to store it!
    UNLESS YOU ARE TRYING TO REPRESENT ZERO
1.01two × 23210
Exponent
Mantissa
Binary point
Radix (Base)
ten

## Slide 9: Scientific Notation (in Binary)
Normalized form has exactly one, non-zero digit to left of binary point
  But in Binary this is always a 1 – We do not need to store it!
    UNLESS YOU ARE TRYING TO REPRESENT ZERO
In computing this is called floating point, because the binary point "floats" up or down to behind the most-significant "1"
1.01two × 23210
Exponent
Mantissa
Binary point
Radix (Base)
ten

## Slide 10: Floating-Point Representation: IEEE 754
±1.x…xtwo × 2y…y
two
1 sign bit
8-bit exponent
23-bit significand
Single precision, FP32 = 32bits
s | y | y | y | y | y | y | y | y | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x

## Slide 11: Floating-Point Representation: IEEE 754
±1.x…xtwo × 2y…y
two
1 sign bit
8-bit exponent
23-bit significand
Single precision, FP32 = 32bits
"Special" values to define denormalised numbers, ±zero, ±infinity, and quiet and signalling not-a-number
s | y | y | y | y | y | y | y | y | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x

## Slide 12: IEEE 754
Standardised by IEEE in 1985
1 sign bit
8-bit exponent
23-bit significand
s | y | y | y | y | y | y | y | y | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
s | y | y | y | y | y | x | x | x | x | x | x | x | x | x | x
s | y | y | y | y | y | y | y | y | y | y | y | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
11-bit exponent
52-bit significand
1 sign bit
1 sign bit
5-bit exponent
10-bit significand
IEEE FP16 = Half precision
IEEE FP32 = Single precision
IEEE FP64 = Double precision

## Slide 13: But this is an arbitrary choice…
“neural networks are far more sensitive to the size of the exponent than that of the mantissa”
1 sign bit
8-bit exponent
23-bit significand
s | y | y | y | y | y | y | y | y | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
s | y | y | y | y | y | x | x | x | x | x | x | x | x | x | x
1 sign bit
5-bit exponent
10-bit significand
1 sign bit
8-bit exponent
7-bit significand
s | y | y | y | y | y | x | x | x | x | x | x | x | x | x | x
IEEE FP16 = Half precision
IEEE FP32 = Single precision
Google bfloat16
Wang and Kanwar, 2019

## Slide 14: Floating point operation
(A × 2a) × (B × 2b)

## Slide 15: Floating point operation
(A × 2a) × (B × 2b) = (A × B) × (2a × 2b) = (A × B) × 2(a + b)
For FP32, that's
1× 8-bit addition 1× 24-bit multiplication

## Slide 16: Floating point operation
(A × 2a) × (B × 2b) = (A × B) × (2a × 2b) = (A × B) × 2(a + b) → (C × 2c)
Renormalisation
For FP32, that's
1× 8-bit addition 1× 24-bit multiplication

## Slide 17: Floating point operation
(A × 2a) × (B × 2b) = (A × B) × (2a × 2b) = (A × B) × 2(a + b) → (C × 2c)
(A × 2a) + (B × 2b)
Renormalisation

## Slide 18: Floating point operation
(A × 2a) × (B × 2b) = (A × B) × (2a × 2b) = (A × B) × 2(a + b) → (C × 2c)
(A × 2a) + (B × 2b) → (A' × 2x) + (B' × 2x) = (A' + B') × 2x
Denormalisation
Renormalisation

## Slide 19: Floating point operation
(A × 2a) × (B × 2b) = (A × B) × (2a × 2b) = (A × B) × 2(a + b) → (C × 2c)
(A × 2a) + (B × 2b) → (A' × 2x) + (B' × 2x) = (A' + B') × 2x → (D × 2d)
Renormalisation
Denormalisation
Renormalisation

## Slide 20: Floating point operation
(A × 2a) × (B × 2b) = (A × B) × (2a × 2b) = (A × B) × 2(a + b) → (C × 2c)
(A × 2a) + (B × 2b) → (A' × 2x) + (B' × 2x) = (A' + B') × 2x → (D × 2d)
The constant need to denormalise and renormalise means that floating point is more costly and has higher latency than integer/fixed point operations
Renormalisation
Denormalisation
Renormalisation

## Slide 21: Cost of Operations
Computing’s Energy Problem (and what we can do about it Horowitz, ISSCC 2014
×9
×1.2

## Slide 22: Cost of Operations
Moving from FP32 to I8 reduces a MAC from 4.6pJ to 0.23pJ
  20-fold energy saving

## Slide 23: Cost of Operations
Moving from FP32 to I8 reduces a MAC from 4.6pJ to 0.23pJ
  20-fold energy saving
Plus gives you 4-fold energy saving on RAM accesses

## Slide 24: Cost of Operations
Moving from FP32 to I8 reduces a MAC from 4.6pJ to 0.23pJ
  20-fold energy saving
Plus gives you 4-fold energy saving on RAM accesses
Plus you can store 4× as many in your local cache

## Slide 25: Fixed point
But nothing comes for free…
Accumulation means that the output is bigger than the input
  And 1.6 trillion parameters means a lot of accumulations
We are free to have a different number of fractional bits in each layer
In hardware, we can choose our number of bits (somewhat) arbitrarily

## Slide 26: Two quantization options
Map |max| to 127
Significant accuracy loss in general

## Slide 27: Two quantization options
Map |max| to 127
Significant accuracy loss in general
Saturate above |threshold| to 127
Weights: no accuracy improvement
Activations: improved accuracy
How do you choose |threshold|?

## Slide 28: How do you choose |threshold|?
Averaging: using a (weighted) average of min/max values of samples in the batch instead of the global min/max
Mean ± Nσ: Take N standard deviation from the mean

## Slide 29: How do you choose |threshold|?
Averaging: using a (weighted) average of min/max values of samples in the batch instead of the global min/max
Mean ± Nσ: Take N standard deviation from the mean
But why bother?

## Slide 30: Quantization-Aware Training
The whole point of a neural network is that training makes it adapt to make the most of it's situation
Make the training aware that the inference is going to be quantized
  “Simulate” quantization effects in the forward pass
  Weights and biases are updated in floating point during backpropagation so that they can be nudged by small amounts
  Typically performs better than post-training quantization

## Slide 31: Impact on Accuracy
Gysel et al., Ristretto, ICLR 2016
Fine-tuned for integer
Without fine-tuning

## Slide 32: Go even smaller… Ternary nets
Ternary Weight Nets (TWN)
  Weights {-w, 0, w}, except first and last layers are 32-bit float
  Activations: 32-bit float
  Accuracy loss: 3.7% on AlexNet
  [Li et al., arXiv 2016]
Trained Ternary Quantization (TTQ)
  Weights {-w1, 0, w2}, except first and last layers are 32-bit float
  Activations: 32-bit float
  Accuracy loss: 0.6% on AlexNet
  [Zhu et al., ICLR 2017]

## Slide 33: Go smaller still… Binary nets
Binary Connect (BC)
  Weights {-1,1}, Activations 32-bit float
  MAC → addition/subtraction
  Accuracy loss: 19% on AlexNet
  [Courbariaux, NeurIPS 2015]
Binarized Neural Networks (BNN)
  Weights {-1,1}, Activations {-1,1}
  MAC → XNOR
  Accuracy loss: 29.8% on AlexNet
  [Courbariaux, arXiv 2016]
Binary Weight Nets (BWN)
  Weights {-α, α}, except first and last layers are 32-bit float
  Activations: 32-bit float
  α determined by the l1-norm of all weights in a filter
  Accuracy loss: 0.8% on AlexNet
XNOR-Net
  Weights {-α, α}
  Activations {-βi, βi}, except first and last layers are 32-bit float
  βi determined by the l1-norm of all activations across channels for given position i of the input feature map
  Scale factors (α, βi) can change per filter or position in filter
  Accuracy loss: 11% on AlexNet
  [Rastegari et al., BWN & XNOR-Net, ECCV 2016]

## Slide 34: Zeros
With integer/fixed point formats, small weights become truly zero

## Slide 35: Zeros
With integer/fixed point formats, small weights become truly zero
RELU has become the activation function of choice
Normalized count
Convolution Layer

## Slide 36: Recall
Accessing DRAM is EXPENSIVE
Accessing DRAM is SLOW
Why bother reading zeros from RAM when they do not contribute to the output?

## Slide 37: Sparse representations
Again – more than one way to skin that cat

## Slide 38: Bitmask Encoding
Using 1-bit/element to indicate whether the value is zero or not.
  Example: NVDLA
Pros: simple and regular
Cons: fixed overhead independent of density
  1/8 overhead for 8-bit values

## Slide 39: Run-Length Encoding
Runs of data (sequences where the same data value, e.g., 0, occurs in consecutive elements) are stored as a single value and count
  Example: Eyeriss
Pros: compression rate linear with #non-zero elements
Cons: overhead: #non-zero × ceil( log2(max. run-length) )

## Slide 40: Compressed-Sparse Column (CSC) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each column (size: #columns)
Row index for each non-zero element within the column (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast column access

## Slide 41: Compressed-Sparse Column (CSC) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each column (size: #columns)
Row index for each non-zero element within the column (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast column access

## Slide 42: Compressed-Sparse Column (CSC) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each column (size: #columns)
Row index for each non-zero element within the column (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast column access

## Slide 43: Compressed-Sparse Column (CSC) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each column (size: #columns)
Row index for each non-zero element within the column (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast column access

## Slide 44: Compressed-Sparse Column (CSC) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each column (size: #columns)
Row index for each non-zero element within the column (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast column access

## Slide 45: Compressed-Sparse Column (CSC) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each column (size: #columns)
Row index for each non-zero element within the column (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast column access

## Slide 46: Compressed-Sparse Column (CSC) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each column (size: #columns)
Row index for each non-zero element within the column (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast column access

## Slide 47: Compressed-Sparse Column (CSC) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each column (size: #columns)
Row index for each non-zero element within the column (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast column access

## Slide 48: Compressed-Sparse Column (CSC) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each column (size: #columns)
Row index for each non-zero element within the column (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast column access

## Slide 49: An aside
This is an example of IMPLICIT information
  You can use *WHERE* the information is within a data-structure to store more information than the amount of memory you use
Compare to EXPLICIT information
  All data is stored explicitly

## Slide 50: Compressed-Sparse Row (CSR) Encoding
Represents a matrix with 3 one-dimension arrays
Bound of each row (size: #rows)
Column index for each non-zero element within the row (size: #non-zero)
Non-zero values (size: #non-zero)
Pros: allow fast row access

## Slide 51: Doubly compressed sparse row/column (DCSR/DCSC) Encoding
Can equivalently store bounds to remove entirely empty rows/columns
DCSR

## Slide 52: Tensor storage format
Can extend the concept to any Tensor (multi-dimensional array)
Separately designate each dimension as dense or sparse
Specify the order in which dimensions are stored
  E.g. CSR is a row-dense, column-sparse format.

## Slide 53: The simplest solution: I/O Compression
For example:
  NVDLA
  Eyeriss (Chen et al., ISSCC 2016)
Matrix operations on uncompressed matrix
Uncompressed
Compressed

## Slide 54: Or you can go hardcore and multiply sparse on sparse
Calculate in parallel which multiplications are non-zero and priority-encode them
SNAP

## Slide 55: Or you can go hardcore and multiply sparse on sparse
SCNN
For CNNs, all non-zero activations must (at some point in time) be multiplied by all non-zero weights
The lack of alignment in IA & W results in a large number of scattered partial sums
Need arbitration logic to send to corresponding output SRAM.

## Slide 56: Pruning – Make Weights Sparse
Example: AlexNet
Weight Reduction: CONV layers 2.7×, FC layers 9.9×
  Most reduction on fully connected layers
Overall: 9× weight reduction, 3× MAC reduction

## Slide 57: Other ways to induce sparsity
Don't reinvent the wheel
  The digital image people have been looking at this stuff for a long time
Exploit Spatial Correlation of Inputs
  Delta code neighbouring values resulting in many zeros for uniform areas
  Works for any activation field, not just input image

## Slide 58: Other ways to save on compute
Don't reinvent the wheel
  The digital video people have been looking at this stuff for a long time
Exploit Temporal Correlation of Inputs
  Reduce amount of computation if there is temporal correlation between frames
  Application specific (e.g. videos) – requires that the same operation is done for each frame (not always the case)

## Slide 59: Exploit Redundant Weights
Repeated weight values get more likely the lower the precision we use
Pre-process to reorder weights
  Ok since weights are known
Perform addition before multiplication to reduce number of multiplies and RAM accesses
Example: Input = [1 2 3] and filter [A B A]
  Typical processing: (A×1) + (B×2) + (A×3)
    3 multiplies and 3 weight reads
  We can reorder to give: (A×(1+3)) + (B×1)
    2 multiplies and 2 weight reads

## Slide 60: Exploit ReLU
If we are using ReLU as our activation function
We can order the weights and inputs by sign so that if the partial sum goes negative the output of ReLU will be guaranteed to be (or be statistically likely to be) 0.
Can terminate accumulation early

## Slide 61: Decompose Convolutions
Break large convolutional layers into a series of smaller convolutional layers
  Fewer weights, but same effective receptive field
After training, perform low-rank approximation by applying tensor decomposition to weight kernel; then fine-tune weights for accuracy

## Slide 62: Decompose Convolutions
For example: AlexNet
  Speed up by 1.6 – 2.7× on CPU/GPU for CONV1, CONV2 layers
  Reduce size by 5 – 13× for FC layer
  <1% drop in accuracy
Particularly effective for low-power processors