## Slide 1: What's going on under the hood of the ML/AI/Big Data revolution?
Andrew W. Rose
Image credit to Sophia Shao @ UC Berkley & Vivienne Sze @ MIT

## Slide 2: It's all about data-structure
It's all about data-structure
  It's all about data-structure
    It's all about data-structure
      It's all about data-structure
        It's all about data-structure
          It's all about data-structure
            It's all about data-structure

## Slide 3: It's all about data-structure
“I will, in fact, claim that the difference between a bad programmer and a good one is whether he considers his code or his data structures more important.
Bad programmers worry about the code.
Good programmers worry about data structures and their relationships.”
Linus Torvalds, 2006

## Slide 4: It's all about data-structure
It's all about data-structure
  It's all about data-structure
    It's all about data-structure
If you want to be fast
  It's all about data-structure
Best-case scenario

## Slide 5: It's all about data-structure
It's all about data-structure
  It's all about data-structure
    It's all about data-structure
If you want to be fast
  It's all about data-structure
If you want to be energy efficient
  It's all about data-structure
Energy to transfer 64 bits (pJ)
Best-case scenario
50×

## Slide 6: It's all about data-structure: Even more important in parallel systems
“The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue, this is a decided disadvantage”
Daniel Slotnick, 1967

## Slide 7: An aside on speed and energy consumption
Pick the right tool for the job
https://greenlab.di.uminho.pt/wp-content/ uploads/2017/10/sleFinal.pdf

## Slide 8: An aside on speed and energy consumption
Pick the right tool for the job
  A real-life example of using Pareto fronts
https://greenlab.di.uminho.pt/wp-content/ uploads/2017/10/sleFinal.pdf
Best
Worst
Python doesn't even make the list

## Slide 9: History
Solving linear maths is a problem as old as computing itself
Old computers were severely resource-limited and optimising the out of the algorithms was the only option
In the 1990's and 2000's, computers ran fast enough that no-one really cared

## Slide 10: History
Solving linear maths is a problem as old as computing itself
Old computers were severely resource-limited and optimising the out of the algorithms was the only option
In the 1990's and 2000's, computers ran fast enough that no-one really cared
But these old tricks are the cornerstone of the AI/ML/Big Data revolution
FORTRAN BLAS library (Basic Linear Algebra Subprograms) implemented GEMM – GEneral Matrix-Matrix Multiplier
… and implemented in all high-performance languages since:
  cBLAS, cuBLAS…

## Slide 11: Fully-Connected (FC) Layer
Input map
Output map
Filters

## Slide 12: Fully-Connected (FC) Layer
Input map
Output map
Filters

## Slide 13: Flattened 2D Dot Product
2D Dot Product
Hadamard Product
Element-wise Product
Entry-wise Product
Schurr Product
1D Dot Product

## Slide 14: Fully-Connected (FC) Layer
Matrix–Vector Multiply:
  Multiply all inputs in all channels by a weight and sum
Input map
Output map
Filter

## Slide 15: Fully-Connected (FC) Layer
Matrix–Vector Multiply:
  Multiply all inputs in all channels by a weight and sum
Input map
Output map
Filter

## Slide 16: Fully-Connected (FC) Layer
Matrix–Vector Multiply:
  Multiply all inputs in all channels by a weight and sum
Input map
Output map
Filter

## Slide 17: Fully-Connected (FC) Layer
Input maps
Output maps
Filters

## Slide 18: Flattened Fully-Connected Layer
After flattening, having a batch size of N turns the matrix-vector operation into a matrix-matrix multiply
Input map
Output map
Filter

## Slide 19: Flattened Fully-Connected Layer
After flattening, having a batch size of N turns the matrix-vector operation into a matrix-matrix multiply
Input map
Output map
Filter

## Slide 20: Flattened Fully-Connected Layer
After flattening, having a batch size of N turns the matrix-vector operation into a matrix-matrix multiply
Input map
Output map
Filter

## Slide 21: Fully-Connected (FC) Layer
After flattening, having a batch size of N turns the matrix-vector operation into a matrix-matrix multiply
How much temporal locality for naïve implementation? None
Input map
Output map
Filter

## Slide 22: Tiled Fully-Connected (FC) Layer
Matrix multiply tiled to fit in cache and computation ordered to maximize reuse of data in cache
Input map
Output map
Filter

## Slide 23: Tiled Fully-Connected (FC) Layer
Matrix multiply tiled to fit in cache and computation ordered to maximize reuse of data in cache
Input map
Output map
Filter

## Slide 24: GEMM
It all comes down to optimizing Matrix Multiplication
  CPU: OpenBLAS, Intel MKL, etc
  GPU: cuBLAS, cuDNN, etc
Library will note shape of the matrix multiply and select implementation optimized for that shape
Optimization usually involves proper tiling to optimize storage hierarchy
Paper here: Anatomy of High-Performance Matrix Multiplication.pdf

## Slide 25: Newer GPUs included dedicated "Tensor Cores"
New opcodes – Matrix Multiply Accumulate (MMA/HMMA/IMMA/DMMA)
  FP16 operands: Inputs 48 / Outputs 16
  Multiplies: 64
  Adds: 64
Tensor Core….
  120 TFLOPS @ FP16
  400 GFLOPS/W @ FP16

## Slide 26: TPU
Top-Level Architecture
Matrix Multiply Unit
Activations
Partial sums
Weights

## Slide 27: Convolution Layer
N× Input maps
N× Output maps
Batch Size (N)
Filters

## Slide 28: Convolution Layer Implementation
Naïve 7-layer for-loop implementation:
For each output map value
Convolve a window
Apply activation

## Slide 29: Convolution Layer
2D Dot Product
1D Dot Product
Input map
Output map
Filter

## Slide 30: Convolution Layer
Convolution
Flattened
Input map
Output map
Filter

## Slide 31: Convolution Layer
Convert to matrix multiply using the Toeplitz Matrix
Convolution
Toeplitz Matrix
Input map
Output map
Filter

## Slide 32: Convolution Layer
Convert to matrix multiply using the Toeplitz Matrix – Data is repeated
Convolution
Toeplitz Matrix
Input map
Output map
Filter

## Slide 33: Convolution Layer
Considering a higher-dimensional convolution – here over 2 channels
Input map
Output map
Filter
Channel 1
Channel 2
Channel 1
Channel 2
Filter 1
Channel 1

## Slide 34: Convolution Layer
Considering a higher-dimensional convolution – here over 2 channels
  Toeplitz still applies
Input map as Toeplitz matrix
Output map
Filter
Channel 1
Channel 2
Filter 1
Channel 1
Channel 1
Channel 2

## Slide 35: Convolution Layer
Considering multiple higher-dimensional convolution – here 2 × 2 channels
Input map
Output map
Filter
Channel 1
Channel 2
Filter 1
Channel 1
Channel 1
Channel 2
Filter 2
Channel 2

## Slide 36: Convolution Layer
Considering multiple higher-dimensional convolution – here 2 × 2 channels
  Toeplitz still applies
Input map as Toeplitz matrix
Output map
Filter
Channel 1
Channel 2
Filter 1
Channel 1
Channel 1
Channel 2
Filter 2
Channel 2

## Slide 37: Generally
For any batch size N, any level of parallelism, any number of input or output channels, we can similarly extend matrices
And GEMM will work it's magic
Input map
Output map
Filter

## Slide 38: Computational Transforms

## Slide 39: Computation Transformations
Goal: Bitwise same result, but reduce number of operations
Focuses mostly on compute

## Slide 40: Gauss’s Multiplication Algorithm
Naïve implementation: 4 multiplications + 3 additions
Optimised: 3 multiplications + 5 additions
1805

## Slide 41: Karatsuba's Algorithm
Apply Gauss' trick for imaginary numbers to multiplying large integers
Recursively split large numbers into numbers half the size using adds, shifts and smaller multiplications
Reduces complexity from O(N2) to O(N1.58)
1960

## Slide 42: Strassen
Naïve implementation: 8 multiplications + 4 additions
Optimised: 7 multiplications + 18 additions
  7 multiplications + 13 additions (for constant B matrix – weights)
1969

## Slide 43: Strassen
Reduce the complexity of matrix multiplication from O(N3) to O(N2.807) by reducing multiplications
Comes at the price of reduced numerical stability and requires significantly more memory
1969
Size, N
Complexity

## Slide 44: Winograd 1D – F(2,3)
Targeting convolutions instead of matrix multiply
Notation: F(size of output, filter size)
Naïve implementation: 6 multiplications + 4 additions
1980

## Slide 45: Winograd 1D – F(2,3)
Targeting convolutions instead of matrix multiply
Notation: F(size of output, filter size)
4 multiplications + 12 additions + 2 shifts
4 multiplications + 8 additions (for constant weights)
1980

## Slide 46: Winograd 2D - F(2x2, 3x3)
1D Winograd is nested to make 2D Winograd
Naïve implementation: 36 multiplications
Winograd: 16 multiplications ≈ 2.25 times reduction
Input map
Output map
Filter
1980

## Slide 47: Optimal convolution algorithm depends on convolution layer dimensions
GoogLeNet – batch size 1
Source: Nvidia

## Slide 48: Winograd Summary
Winograd is an optimized computation for convolutions
It can significantly reduce multiplies
  For example, for 3x3 filter by 2.25X
But, each filter size and output size is a different computation
Paper here: Fast Algorithms for Convolutional Neural Networks.pdf

## Slide 49: Winograd as a Transform
Input map
Filter
Transformed filter GgGT can be precomputed
Transform Input
Element-wise

## Slide 50: And if we are going to talk about transforms…
The most famous transformation of the 20th and 21st centuries
The Fast Fourier Transform/Discrete Fourier Transform

## Slide 51: Fast Fourier Transform (FFT)
Input map
Output map
Filter

## Slide 52: FFT Overview
Convert filter and input to frequency domain to make convolution a simple multiply then convert back to space domain.
Convert direct convolution O(No2Nf2) computation to O(No2log2No)
The computational benefit of FFT increases with increasing size of filter
  Or decreases with decreasing size of filter

## Slide 53: But nothing comes for free…
Input and Filter matrices are ‘0-completed’
  i.e. expanded to size (E+R-1) × (F+S-1)
Frequency domain matrices are same dimensions as input, but complex
FFT often reduces computation, but requires much more memory space and bandwidth

## Slide 54: Optimization opportunities
FFT of real matrix is symmetric allowing one to save ½ the computes
Filters can be pre-computed and stored, but convolutional filter in frequency domain is much larger than in space domain
Can reuse frequency domain version of input for creating different output channels to avoid FFT re-computations
Can accumulate across channels before performing inverse transform to reduce number of IFFT

## Slide 55: cuDNN: Speed up with Formalised Transforms
AlexNet training throughput
Source: Nvidia
60× speed-up in 3 years
And recall, V100 is 4-9× faster than P100 for Matrix maths because of its Tensor core

## Slide 56: It's all about data-structure: Even more important in parallel systems
Didn't have time to go into it today but I'll assert it again…
“The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue, this is a decided disadvantage”
Daniel Slotnick, 1967

## Slide 57: Conclusion
The last 75 years have seen many developments in optimisation of linear maths
  And it (mostly) comes down to data-structure
More recently the idea of formalized transforms have optimised the parallelization of linear maths on GPUs
And the same tricks apply equally to other parallelised hardware
  But even more important
The introduction of dedicated tensor cores hasn't hurt