## Slide 1: An introduction to FPGAs and spatially-pipelined computing
Andrew W. Rose
Imperial College, London

## Slide 2: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS Raw
CMS Zero-suppressed
Tape storage
Five orders of magnitude

## Slide 3: The Level-1 trigger problem
The CMS Level-1 trigger handles ~10Tb of data per second
Or ~ 250kb of data per event

## Slide 4: What is so hard about that?
So…

## Slide 5: So what is so hard… how processors work

## Slide 6: So what is so hard… how processors work
Stop and Reload
Have a cup of tea
Biscuit, anyone?

## Slide 7: So what is so hard… how triggers work
The data keeps on coming, whether you are ready or not
Like one of those tennis machines, except that missing a ball means losing your Nobel prize winning Higgs/SUSY discovery
Slow
Med
Fast
LHC

## Slide 8: So what is so hard… how triggers work
The data keeps on coming, whether you are ready or not
Like one of those tennis machines, except that missing a ball means losing your Nobel prize winning Higgs/SUSY discovery
Slow
Med
Fast
LHC

## Slide 9: Evolution of Microelectronics

## Slide 10: How to perform logical operations
Valve transistors
Solid-state transistors
First
solid-state transistors

## Slide 11: How to perform logical operations
First
multi-transistor
silicon
Packaged Logic
“Mini” processor board

## Slide 12: How to perform logical operations
Application Specific Integrated Circuit (ASIC)
$
Qty
ASIC
Programmable Logic
APV25 - Imperial College, London

## Slide 13: Two philosophies: Space vs. Time
Have each operation performed by dedicated logic and do that same operation on every clock cycle
Have each operation performed by the same logic, performing a different operation on every clock cycle
“The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue, this is a decided disadvantage”
Daniel Slotnick, 1967
Sequential
Parallel

## Slide 14: And the story diverges…
Programmable Array Logic
Microprocessor
Pack entire logic circuits in a chip
Perform all logical operations in one location, but sequentially
Limited further discussion of microprocessors

## Slide 15: Sum-of-products theorem
Any Boolean operation may be expressed as
the OR of AND operations (Sum of products form)
Or
the AND of OR operations (Product of sums form)
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 16: Programmable Logic Devices (PLDs)
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
Unprogrammed
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 17: Programmable Logic Devices (PLDs)
Programmed
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 18: Programmable Logic Devices (PLDs)
Originally one-time programmable
Later field reprogrammable
What did people do? Build boards with many PLDs…
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 19: Complex PLDs (CPLDs)
Feedback
Feedback
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 20: Programmable Interconnect matrix

## Slide 21: An alternative approach
While this was happening, SRAM was also evolving!
Why bother with the complexity of the PLD cell?
Replace the PLD cell with a simple SRAM:
  Data-in becomes the “address”
  Outputs the preloaded value for a given input
The Field Programmable Gate Array
(FPGA)

## Slide 22: Field Programmable Gate Arrays (FPGAs)
‘Simple’ Programmable Logic Blocks
Massive Fabric of Programmable Interconnects
Notes: A field-programmable gate array (FPGA) is a large-scale integrated circuit that can be programmed after it is manufactured rather than being limited to a predetermined, unchangeable hardware function. The term "field-programmable" refers to the ability to change the operation of the device "in the field," while "gate array" is a somewhat dated reference to the basic internal architecture that makes this after-the-fact reprogramming possible.

## Slide 23: What’s the difference?
Standard CMOS Integrated Circuit fabrication process as for SRAM memory chips
Take maximum advantage of Moore’s Law!

## Slide 24: Evolution of features in FPGAs

## Slide 25: Xilinx 7-series Combinatorial Logic Block
Smarter than your average LUT

## Slide 26: Xilinx 7-series Digital Signal Processing (DSPs)
“Logic cells for doing maths”
XC7VX690T has 3600 DSPs ≈ 1.8 billion Multiply-Accumulates/second

## Slide 27: I/O
Traditionally, many hundreds of general purpose pins (Gen I/O) up to a few hundred MHz
Latest generation Gen I/O up to 1.8Gbps
Programmable logic standards
Since 2002, FPGAs have been adding dedicated Multi-gigabit transceivers
Arms race - Ever more and ever faster

## Slide 28: Biggest Parts Virtex 7
28Gb/s
2.8 Tb/s – Blimey!
(280,000×
ADSL 10Mb connections)

## Slide 29: IC processing cards for CMS calo trigger
Bandwidth
Logic

## Slide 30
Backplane has low latency LVDS IO as well as standard SerDes (e.g. GbE, PCIe, etc.)
30×
1.8 Gbps
low-latency LVDS IO
Optical mounts (6Rx + 6Tx)
× 12-channels @ 14G
Xilinx Virtex-7 FPGA
Up to 80+80 13G

## Slide 31
Transmitters
Transmitters
Receivers
Receivers
FPGA
2v5
3v3
1v0
1v5
1v8
Header

## Slide 32
Microcontroller for crate & power management
32GB μSD Card acts as PROM.
Fast write capability.
Can store all firmware versions
USB2 for console / debug
Standard PROM for inviolate boot images

## Slide 33
A1v0
A1v2
A1v0
A1v2
QDR
QDR
CPLD
μC
Clk
USB
μSD
Clocking

## Slide 34: Recall…
PALs / PLDs / FPGAs
Microprocessors
Parallel operations across many locations
Sequential operations in one location
Can’t use “normal” programming languages like C/C++

## Slide 35: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
That would just be stupid

## Slide 36: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 37: Hardware Description Languages
Need a language to describe hardware
Novelly – called a “Hardware Description Language” (HDL)
Also called FIRMWARE
Two popular languages are VHDL , VERILOG
Easy to start learning… Hard to master!
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 38: Hardware Description Languages
Describe Logic as collection of Processes operating in Parallel
Language Constructs for Synchronous Logic
Compiler (Synthesis) Tools recognise certain code constructs and generates appropriate logic
Not all constructs can be implemented in FPGA!
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 39: Example
architecture behavioural of test is
begin
process(x, y)
begin
-- compare to truth table
if ((x='1') and (y='1')) then
F <= '1';
else
F <= '0';
end if;
end process;
G <= x or y;
end behavioural;
library ieee;
use ieee.std_logic_1164.all;
entity test is
port(
x: in std_logic;
y: in std_logic;
F: out std_logic;
G: out std_logic);
end test;
Must write code with
understanding of how
it will be implemented.
Can also enter code via schematic entry:
  Easier to navigate, but not vendor independent
  Will there ever be a standard graphical programming language?

## Slide 40: How to you know it works?
Simulate design extensively!
  Much quicker than debugging inside the FPGA

## Slide 42: Testbench Suite
“Event display”

## Slide 43: Testbench Suite
Clock-by-clock summary
End-of-event summary

## Slide 44: Designing Logic with FPGAs
High level Description of Logic Design (HDL)
Synthesise into a Netlist
  Boolean Logic Representation
Target FPGA Device
  Translate
  Mapping
  Routing
Bit File for FPGA
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 45: Configuring an FPGA
Millions of SRAM cells holding LUTs and Interconnect Routing
Volatile Memory: Lose configuration when board power is turned off.
Keep bit patterns describing the SRAM cells in non-Volatile Memory e.g. PROM or memory card
Configuration takes ~ secs
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 46: It doesn’t work: How to debug
Simulate, simulate & simulate again!
  Much quicker than debugging inside the FPGA
Route out signal to periphery
  Few debug pins always handy
  Can connect UART for uC debug (StdIn/StdOut)
Use chipscope
  Rebuild design with embedded logic analyser
    Can be a bit like quantum mechanics
    If you look (i.e. make a measurement) your code can behave differently
    Chipscope presence can affect the original design

## Slide 47: Floorplan of firmware in MP7

## Slide 48: Floorplan of firmware in MP7
Communication
DAQ
(work in progress)
MGTs and DAQ buffers
MGTs and DAQ buffers
Algorithms

## Slide 49: When & why should I (not) use an FPGA?
FPGAs are expensive (high-end £10k-100k cf. £100)
FPGAs are power-hungry
Programming FPGAs is like designing logic circuits not like programming sequential microcontrollers
Large firmware build-times are tens of hours or days
Floating-point ops and iterative algorithms awkward in FPGAs (That said, you “control” the silicon, so, of course, it can be done)
FPGAs best for high through-put, low- and/or fixed-latency operations

## Slide 50: Conclusion
FPGAs are intrinsically parallel
Modern FPGAs are exceptionally powerful
FPGAs are a monumental PAIN IN THE BACKSIDE to program
  Partly due to the clunky, verbose HDLs
  Mainly due to the difficulty of conceptualizing massively parallel logic and pipelined logic
Get them right and you can do magic
Get them wrong and you unleashed a world of pain on yourself

## Slide 51: Spares

## Slide 52: Up against the speed of light…
Wait for the signal to propagate
“Sea-of-logic” approach
Limits clock speed
Do less each clock-cycle
Compensated for by much higher clock speeds

## Slide 53: Recall: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 54: Full pipelining
If you want to get the most out of your FPGA, you need to pipeline at the full data-rate (6 or more times higher than the LHC BX clock)
Design your system to achieve this!
A lot of people still don’t get this…

## Slide 55: Conventional trigger
Data is processed in regions
Boundaries between regions must be handled by sharing or duplicating inputs
Volume of data reduced at each stage by selecting and discarding candidates
When volume of data has been sufficiently reduced it can be passed to the global trigger

## Slide 56: Time-multiplexed trigger
Data from an event is buffered and retransmitted to the first processing node over N bunch crossings
Data from the next event is buffered and retransmitted to the second processing node, again, over N bunch crossings
Process is repeated in round-robin fashion across ≥N processing nodes
Because both algorithm latency and data volume are constant, dataflow is fully deterministic and no complex scheduling mechanism is required