## Slide 1: The LHC and the really big data challenge
Instrumentation course guest lecture
Andrew W. Rose, Imperial College London
awr01@imperial.ac.uk

## Slide 2: Introduction
I hope you will all be familiar to some extent with the Large Hadron Collider at CERN, Switzerland but will assume minimal background knowledge
The largest and most complex scientific endeavour in history
Most famous for its observation of the Higgs boson

## Slide 3: Science: The basics
A bold statement:
Science is the art of knowing
what to record, and when

## Slide 4: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
Ten orders of magnitude

## Slide 5: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building

## Slide 6: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building
  Or if you collided protons once per second, that is one event every 317 years

## Slide 7: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building
  Or if you collided protons once per second, that is one event every 317 years
And one Higgs boson is pretty much USELESS We need loads of them to be able to study them…

## Slide 8: This is why the LHC collides…
̴50 protons at a time × 40 million times a second

## Slide 9: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds

## Slide 10: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
But this causes problems

## Slide 11: One proton-proton collision

## Slide 12: Many proton-proton collisions
25 proton-proton collisions

## Slide 13: Many proton-proton collisions
25 proton-proton collisions
Even if you get a Higgs boson, the RUBBISH makes it hard to find

## Slide 14: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
This causes other problems too

## Slide 15: Single Event Upsets
When energetic charged particles pass through a transistor, they can change the state
  And there are plenty of charged particles in the LHC experiments

## Slide 16: Single Event Upsets
When energetic charged particles pass through a transistor, they can change the state
  And there are plenty of charged particles in the LHC experiments
In a microprocessor
  At best this corrupts the data
  At worst it changes the program flow

## Slide 17: Single Event Upsets
When energetic charged particles pass through a transistor, they can change the state
  And there are plenty of charged particles in the LHC experiments
In a microprocessor
  At best this corrupts the data
  At worst it changes the program flow
There are much, much worse effects
  Entire circuits reconfigured
  Transistor shorts power to ground – burn out the chip
  Block the ability to reset or reconfigure the chip

## Slide 18: Single Event Upsets
Mitigate by having three copies of the logic and arbitrate by majority logic
  Triple Redundant Logic
Deep well transistor architectures to minimize charge collection
Insulating substrates rather than semiconductors
  Diamond, Sapphire, …
Or wide band gap substrates
  Silicon Carbide, Gallium Nitride
Continual reconfiguration
  Called "Scrubbing"
Designing radiation-hard electronics is a specialist skill

## Slide 19: Single Event Upsets
Mitigate by having three copies of the logic and arbitrate by majority logic
  Triple Redundant Logic
Deep well transistor architectures to minimize charge collection
Insulating substrates rather than semiconductors
  Diamond, Sapphire, …
Or wide band gap substrates
  Silicon Carbide, Gallium Nitride
Continual reconfiguration
  Called "Scrubbing"
The best solution is to keep your most sensitive electronics as far away from radiation as possible

## Slide 20: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
But this causes problems
This causes problems too

## Slide 21: Big detectors for small particles

## Slide 22: Big detectors…
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers

## Slide 23: Big detectors…
~65M Silicon Pixels
~10M Silicon Strips
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers
~80k PbWO4 Ecal Crystals
× 40 million measurements per second

## Slide 24: … Bigger data
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
~80k PbWO4 Ecal Crystals ≡ 40 TBit per second
× 40 million measurements per second

## Slide 25: … Bigger data
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
~80k PbWO4 Ecal Crystals ≡ 40 TBit per second
What does that even mean?

## Slide 26: What does that even mean?
https://www.cisco.com/
×200
×50

## Slide 27: What does that even mean?
https://arxiv.org/pdf/2202.07659.pdf
The amount of data being produced

## Slide 28: What does that even mean?
https://arxiv.org/pdf/2202.07659.pdf
The amount of data we can store
The amount of data being produced

## Slide 29: What does that even mean?
But do we need to store it all?
The Higgs is rare, after all
https://arxiv.org/pdf/2202.07659.pdf

## Slide 30: So what do we do?
We keep the data safe on the detector

## Slide 31: So what do we do?
We keep the data safe on the detector
Designing radiation-hard electronics is a specialist skill
CMS CBC3 ASIC Designed at Imperial College London Layout at Rutherford Appleton Lab

## Slide 32: So what do we do?
We keep the data safe on the detector for several microseconds

## Slide 33: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some small fraction of the data and select the interesting crossings to keep

## Slide 34: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some small fraction of the data and select the interesting crossings to keep
Called Triggering

## Slide 35: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some small fraction of the data and select the interesting crossings to keep
Called Triggering
uninteresting crossings to discard
The LHC is a discovery machine, after all

## Slide 36: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some small fraction of the data and select the interesting crossings to keep
Called Triggering
The LHC is a discovery machine, after all
~30Tbps
uninteresting crossings to discard

## Slide 37: But!
If you get it wrong
If your system fails you throw away your valuable physics
If you take too long

## Slide 38: But!
If you get it wrong
If your system fails you throw away your valuable physics
If you take too long
And that is a *really, really* expensive mistake

## Slide 39: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some small fraction of the data and select the interesting crossings to keep

## Slide 40: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some small fraction of the data and select the interesting crossings to keep
But the radiation in the experiment is so intense that the programmable electronics is kept 100m away
The speed of light costs you 1μs to get the data off detector
And 1μs to get the decision back to the detector
Leaves 1.2μs for all data processing

## Slide 41: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some small fraction of the data and select the interesting crossings to keep
But the radiation in the experiment is so intense that the programmable electronics is kept 100m away
The speed of light costs you 1μs to get the data off detector
And 1μs to get the decision back to the detector
Leaves 1.2μs for all data processing
4800 instructions on a 4GHz CPU

## Slide 42: But recall…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
But this causes problems
This causes other problems too

## Slide 43: A note on timescales
At 40MHz BX rate, a 4GHz CPU could perform 100 CPU operations (not enough to be useful) before the next data arrives
What technology can we use?

## Slide 44: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 45: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 46: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
That would just be stupid

## Slide 47: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
That would just be stupid
But this is essentially what a PC does

## Slide 48: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 49: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
So why doesn’t my PC do this?

## Slide 50: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
Because writing code like this is *really, really* hard
So why doesn’t my PC do this?

## Slide 51: What technology can we use?
Application-specific integrated circuits (ASICs): design encoded into silicon
Field-programmable gate arrays (FPGAs)

## Slide 52: Field-Programmable Gate Arrays
Programmable circuit-on-chip

## Slide 53: Field-Programmable Gate Arrays
Programmable circuit-on-chip
Upwards of 9 million logic cells & up to 12000 “math” cells
  All clocked at ̴500MHz
Up to O(1015) operations/second
Fully parallel and fully pipelineable

## Slide 54: Field-Programmable Gate Arrays
Programmable circuit-on-chip
Upwards of 9 million logic cells & up to 12000 “math” cells
  All clocked at ̴500MHz
Up to O(1015) operations/second
Fully parallel and fully pipelineable
Rather useful when you are dealing with 30Tbps

## Slide 55: Field-Programmable Gate Arrays
Programmable circuit-on-chip
Upwards of 9 million logic cells & up to 12000 “math” cells
  All clocked at ̴500MHz
Up to O(1015) operations/second
Fully parallel and fully pipelineable
Rather useful when you are getting new data every 25ns

## Slide 56: Field-Programmable Gate Arrays
Programmable circuit-on-chip
Upwards of 9 million logic cells & up to 12000 “math” cells
  All clocked at ̴500MHz
Up to O(1015) operations/second
Fully parallel and fully pipelineable
Rather useful when you are dealing with 30Tbps
Rather useful when you are getting new data every 25ns
and *really, really* hard to program efficiently

## Slide 57: The CMS Calorimeter trigger
Clusters combination Filtering Sums
Seeding & basic clustering
Inputs
Unpack & Linearisation
EG/TAU/Jets PileUp
Outputs
Isolation&Calibration
Sort
Cumulative sort
Jet building with pileup subtraction
Dynamic clustering
Shape veto, H/E, isolation, calibration
72 × 10 Gbps links
720 Gbps
2.3kb per 25ns

## Slide 58: The CMS Calorimeter trigger
Clusters combination Filtering Sums
Seeding & basic clustering
Inputs
Unpack & Linearisation
EG/TAU/Jets PileUp
Outputs
Isolation&Calibration
Sort
Cumulative sort
Jet building with pileup subtraction
Dynamic clustering
Shape veto, H/E, isolation, calibration
Each box itself consists of a number of pipelined operations
72 × 10 Gbps links
720 Gbps
2.3kb per 25ns

## Slide 59: What type of algorithms are we talking about?
Classical algorithms
  Clustering in 2D or 3D
  Pattern identification/matching
  Kalman filtering
Remember that they have to be implemented in a fully parallel and
fully pipelined
form

## Slide 60: What type of algorithms are we talking about?
Classical algorithms
  Clustering in 2D or 3D
  Pattern identification/matching
  Kalman filtering
In future
  Particle-flow – full reconstruction of particles and events
  Machine-learning, BDTs and neural-nets in chip
Remember that they have to be implemented in a fully parallel and
fully pipelined
form

## Slide 61: Field-Programmable Gate Arrays
A chip needs to be attached to something!
Imperial’s latest platform: Serenity

## Slide 62: Field-Programmable Gate Arrays
A chip needs to be attached to something!
Imperial’s latest platform: Serenity
  208 optical transmit links & 208 optical receive links @ 28.5Gbps =
  Skewable to
5.9 + 5.9 Tbps
7.0 + 4.8 Tbps

## Slide 63: Field-Programmable Gate Arrays
A chip needs to be attached to something!
Imperial’s latest platform: Serenity
A real challenge:
30Gbps links requires ~analogue design
Each chip drawing over 100A of core power
Heat management a huge challenge
  6 ground planes – need to control noise
  4 power planes – need to supply 9 voltages per chip at up to 100A
  6 signal layers – these are big chips

## Slide 64: The future: High-luminosity LHC
Up to 250 proton-proton collisions per event
Really, really hard to find the interesting event under all that rubbish
Need to sift through 300Tbps to find the interesting events
150 proton-proton collisions

## Slide 65: Conclusion
To find the interesting events at the LHC we must search through vast amounts of data

## Slide 66: Conclusion
To find the interesting events at the LHC we must search through vast amounts of data
To do this requires work at the cutting edge of electronics, programming and physics

## Slide 67: Conclusion
To find the interesting events at the LHC we must search through vast amounts of data
To do this requires work at the cutting edge of electronics, programming and physics
  And in the future, also Machine Learning

## Slide 68: Conclusion
To find the interesting events at the LHC we must search through vast amounts of data
To do this requires work at the cutting edge of electronics, programming and physics
  And in the future, also Machine Learning
And this will be even more challenging at the HL-LHC
  Lots of fun to be had

## Slide 69: Thanks for listening
Any questions?

## Slide 70: Spares

## Slide 71: How much data?
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
1× Home broadband
1,000,000× Home broadband
1,000× Home broadband
CMS Raw
CMS tape-store

## Slide 72: Layered triggers
In our FPGAs we accept events at 100kHz (out of the 40MHz)
  Reduced the total data volume by a factor of 400
Small enough to get through an ethernet network into PCs

## Slide 73: Layered triggers
In our FPGAs we accept events at 100kHz (out of the 40MHz)
  Reduced the total data volume by a factor of 400
Small enough to get through an ethernet network into PCs
  Although, of course, "small" here is relative
100 kHz
~13000 CPU cores

## Slide 74: Spares: Introduction to detectors

## Slide 75
ONE DOES NOT SIMPLY
SEE A HIGGS BOSON

## Slide 76: Heavy and unstable
If a heavy and unstable state is produced by a proton-proton collision, it decays quickly into more stable particles

## Slide 77: Heavy and unstable
If a heavy and unstable state is produced by a proton-proton collision, it decays quickly into more stable particles
And I mean REALLY quickly:
Doesn't get anywhere near a detector
Higgs Boson | 1.6 × 10-22 seconds
W/Z Boson | 3 × 10-25 seconds
Top Quark | 5 × 10-25 seconds
Tau Lepton | 2.9 × 10-13 seconds

## Slide 78: So we can't see the Higgs (or most other particles) directly
But you can't "see" the other particles either (in a conventional sense)
So how are particle detectors built?

## Slide 79: A parallel question
How can you tell the properties of a car and how fast it is going from the outside?

## Slide 80: Minimal disruption
Take a couple of snapshots
Work out how it got between them and how long it took to do so

## Slide 81: Minimal disruption
Take a couple of snapshots
Work out how it got between them and how long it took to do so
Does not affect the speed/momentum/energy of the car

## Slide 82: Minimal disruption
Lightweight tracker that records the position of charged particles as accurately as possible, while affecting the particle as little as possible

## Slide 83: Minimal disruption
Lightweight tracker that records the position of charged particles as accurately as possible, while affecting the particle as little as possible
Join-the-dots
Apply a magnetic field to determine the charge and momentum

## Slide 84: Maximal disruption
Place something very heavy in the way
Collect all the bits; measure how far the pieces get thrown
Certainly does affect the speed/momentum/ energy of the car

## Slide 85: Maximal disruption
Put something very dense in the way
  Brass
  Steel
  Tungsten
  Depleted uranium
  Lead tungstate crystals
Catch the light in some transparent medium using photomultipliers

## Slide 86: Maximal disruption
Energetic leptons particles emit photons
  Energetic photons pair-produce electrons and positrons
    Which emit photons
      Which pair-produce electrons and positrons
        Which emit photons
          Which pair-produce electrons and positrons
            Which emit photons…
Energetic hadrons break up into lighter hadrons
  Which break up into lighter hadrons
    Which break up into lighter hadrons
      Which break up into lighter hadrons…
  Pions decay to photons
    Which pair-produce electrons and positrons…
      Which emit photons…

## Slide 87: The CMS detector
Particles collide here

## Slide 88: The CMS detector
Pixel and strip trackers

## Slide 89: The CMS detector
Calorimeters

## Slide 90: The CMS detector
4T superconducting magnet

## Slide 91: The CMS detector
Muon trackers

## Slide 92: Event reconstruction
Join the tracks with the energy deposits
Apply energy and momentum conservation to reconstruct everything all the way down to the interaction point

## Slide 93: Spares: Introduction to triggers

## Slide 94: Reminder
Trigger basic requirements
  Need high efficiency for selecting processes for physics analysis
  Need large reduction of rate from unwanted high-rate processes
  Robustness is essential
  Highly flexible, to react to changing conditions
  System must be affordable

## Slide 95: The earliest trigger
Cloud-chamber images recorded on film
Need some way to trigger the camera

## Slide 96: The earliest trigger
Cloud-chamber images recorded on film
Need some way to trigger the camera
Grad student
†Artist’s impression

## Slide 97: The earliest trigger
High efficiency? Nope – reflexes too slow
Large rate reduction? Better than nothing
Robustness? No – keep wanting sleep, coffee, toilet breaks, etc.
Highly flexible? Depends on the student
Grad student
†Artist’s impression

## Slide 98: The earliest trigger
High efficiency? Nope – reflexes too slow
Large rate reduction? Better than nothing
Robustness? No – keep wanting sleep, coffee, toilet breaks, etc.
Highly flexible? Depends on the student
Affordable? Well that’s one thing in your favour, I suppose
Grad student
†Artist’s impression

## Slide 99: The earliest trigger
High efficiency? Nope – reflexes too slow
Large rate reduction? Better than nothing
Robustness? No – keep wanting sleep, coffee, toilet breaks, etc.
Highly flexible? Depends on the student
Affordable? Well that’s one thing in your favour, I suppose
Grad student
†Artist’s impression
  Although Rutherford & Geiger did note that “Strong coffee with a pinch of Strychnine” improved the ability to spot scintillation light

## Slide 100: The earliest trigger
Blackett pioneered a technique to trigger the camera of cloud chambers (and got the Nobel prize for this and other work)
Just missed out on discovering the positron in 1932
Stevenson and Street used this to confirm the discovery of the muon in 1937

## Slide 101: The simplest trigger systems
Source: Use the signals from the Front-End of the detectors themselves
  Binary: tracking detectors (pixels, strips)
  Analog: tracking detectors, time of flight detectors, calorimeters, …
Front-End
Pre-amplifier
Amplifier

## Slide 102: The simplest trigger systems
Source: Use the signals from the Front-End of the detectors themselves
  Binary: tracking detectors (pixels, strips)
  Analog: tracking detectors, time of flight detectors, calorimeters, …
The most trivial trigger algorithm: Signal > Threshold
  Apply the lowest possible threshold
  Identify best compromise between hit efficiency and noise rate
Source
Trigger signal
Discriminator
Accept
Reject
Front-End
Pre-amplifier
Amplifier

## Slide 103: Detector signals characteristics
Leading edge
Trailing edge
Pulse width
  Limits the effective hit rate
  Must be adapted to the desired trigger rate
Time walk
  The threshold-crossing time depends on the signal amplitude
  Must be minimal good trigger systems
Time walk can be suppressed by triggering on total signal fraction
  Applicable on same-shape input signals with different amplitude
  Scintillator detectors and photomultipliers

## Slide 104: The constant fraction discriminator
  Attenuation + configurable delay applied before the discrimination determines tCFD
  If delay too short, the unit works as a normal discriminator since the output of the normal discriminator fires later than the CFD part
Input pulse
Delayed input pulse
Attenuated inverted input
Bipolar pulse
The output of the CFD fires when the bipolar pulse changes polarity
at t = tcfd
Signals with the same rising time, at a fraction f

## Slide 105: Trigger logic implementation
Once we are in the digital domain, all manipulations can be broken down to a Boolean operations
Combinatorial
  Summing, Decoders, Multiplexers,…
Sequential
  Flip-flops, Registers, Counters,…
AND
OR
NOT

## Slide 106: Trigger logic implementation
Once we are in the digital domain, all manipulations can be broken down to a Boolean operations
Combinatorial
  Summing, Decoders, Multiplexers,…
Sequential
  Flip-flops, Registers, Counters,…
AND
OR
NOT
Data propagates as a wave through the logic
Operations happen at well defined times and in a well defined order

## Slide 107: A simple trigger system
Detector
discriminators
coincidence logic
Front-Ends
start
delays
Digitizers (ADC, TDC,….)
busy
Trigger system
&
ReadOut
FE
FE
FE
FE
Fast links

## Slide 108: DeadTime
The key parameter in high speed trigger systems design
  The fraction of the acquisition time when no events can be recorded.
  Typically of the order of few %
  Reduces the overall system efficiency
Arises when a given processing step takes a finite amount of time
  Readout dead-time
  Trigger dead-time
  Operational dead-time

## Slide 109: Deadtime Example
Writing to disk or tape is much slow than accepting data into RAM
If you select an event and start writing it to disk, you cannot accept any more events until you finish writing, even if they are interesting

## Slide 110: Deadtime example
For input rate, “Rin”, Readout rate, “Rout”, and time taken to write to disk, “Td”
Fraction of lost events = Rout•Td
Event output rate Rout = (1-Rout•Td)•Rin
Rout(Hz)
Rin(Hz)
Td=1s
Td=2s
  for Td = 1s →max rate = 1Hz
IRREDUCIBLE!!!
Fraction of surviving events
To achieve high efficiency ⟹

## Slide 111: Deadtime
Writing to disk or tape is much slow than accepting data into RAM
If you select an event and start writing it to disk, you cannot accept any more events until you finish writing, even if they are interesting
Same principle applies to processing time
  For example, ADCs

## Slide 112: A simple trigger system: Deadtime
discriminators
coincidence logic
Front-Ends
start
delays
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADC

## Slide 113: A simple trigger system: Deadtime
Detector
discriminators
coincidence logic
Front-Ends
start
delays
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADC
If ADC is the critical step for deadtime, this is clearly a really bad plan

## Slide 114: A simple trigger system: Parallelism
Detector
discriminators
coincidence logic
Front-Ends
start
delays
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Much more sensible!
Potentially much more expensive!
  Independent readout and trigger paths, one for each sensor element
  Digitisation and DAQ processed in parallel (as much as affordable!)

## Slide 115: A simple trigger system: Latency
discriminators
coincidence logic
Front-Ends
delays
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
  Latency: Time to form the trigger decision and distribute to the digitisers
  Signals must be delayed until the trigger decision is available
  The more complex is the selection, the longer is the latency

## Slide 116: A simple trigger system: Latency
discriminators
coincidence logic
Front-Ends
delays
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Analogue delay-lines are a bit risky, don’t you think?
Especially for more than one channel

## Slide 117: A simple trigger system: Pre-trigger
discriminators
coincidence logic
Front-Ends
start
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Pre-trigger
Start ADC
  Pre-Trigger stage: very fast indicator of some minimal activity in the detector
  Used to START the digitisers, with no delay
  The complex trigger decision comes later

## Slide 118: A simple trigger system: Pre-trigger
discriminators
coincidence logic
Front-Ends
start
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Pre-trigger
Start ADC
Assumes the digitization time is longer than the latency of the trigger system!
What if that is not true?

## Slide 119: A simple trigger system: Pre-trigger
discriminators
coincidence logic
Front-Ends
start
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Pre-trigger
Start ADC
Digital delay
A PIPELINE
Since each digitization takes a finite time
Can store the result of each digitization in RAM until trigger decision is made
Data Valid

## Slide 120: Simple trigger system: Bunched Colliders
discriminators
coincidence logic
start
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Front-Ends
We have a master-clock – the bunch-crossings themselves!
No need for a pre-trigger
Digital delay
A PIPELINE

## Slide 121: A Simple trigger system: Digital Triggers
start
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Front-Ends
Digital delay
A PIPELINE
Digital Trigger system

## Slide 122: A Simple trigger system: Digital Triggers
start
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Front-Ends
Digital delay
A PIPELINE
Digital Trigger system
  This is the fundamental design behind all modern collider trigger-systems

## Slide 123: A trigger system: Multilayer Triggers
Accept
FE
FE
FE
FE
Fast links
ReadOut
ADCs
Front-Ends
Digital delay
A PIPELINE
Digital Trigger system
Accept
Filter
Filter
Digital Trigger system
Digital delay
A PIPELINE

## Slide 124: Multilayer triggers
Each stage reduces the rate, so later stages have longer latency
Complexity of algorithms increases at each level
Dead-time is the sum of the trigger dead-time, summed over the trigger levels, and the readout dead-time
Pre-trigger: i=1

## Slide 125: MultiLAYER triggers
Adopted in large experiments
  More and more complex algorithms are applied on lower and lower data rates
Efficiency for the desired physics must be kept high AT ALL LEVELS, since rejected events are lost for ever
LHC experiments @ Run1 | 
Experiment | Number of Levels (excl. analysis)
ATLAS | 3
CMS | 2
LHCB | 3
ALICE | 4
Level-1
Level-2
Level-3
Analysis
Longer latency
Lower event rate
Larger event fragment size
Higher algorithmic complexity
Access to higher granularity information
Low latency
Full event rate
Small event fragment size
Lower algorithmic complexity
Access to coarse granularity information

## Slide 126: A trigger system: Multilayer Triggers
Accept
FE
FE
FE
FE
Fast links
ReadOut
ADCs
Front-Ends
Digital delay
A PIPELINE
Digital Trigger system
Accept
Filter
Filter
RAM
If your input rate is low enough

## Slide 127: A trigger system: Multilayer Triggers
And this is exactly what the CMS Trigger does
“Standard” figure for the CMS Trigger & DAQ

## Slide 128: Of course, “Low enough” is relative…

## Slide 129: Synchronous or asynchronous?
Synchronous: operates phase-locked with master clock
  Data move in lockstep with the clock through the trigger chain
  Fixed latency
  The data, held in storage pipelines, are either sent forward or discarded
  Used for L1 triggers in collider experiments, exploiting the accelerator bunch crossing clock
  Pro’s: dead-time free (just few clock cycles to protect buffers)
  Con’s: cost (high frequency stable electronics, sometimes needs to be custom made); maintain synchronicity throughout the entire system, complicated alignment procedures if the system is large (software, hardware, human…)
T1
T4
T3
T2
FE buffers
Local
trigger decision
Global trigger decision going back to FE
FE data
to the DAQ
YES
data
Fixed time

## Slide 130: Synchronous or asynchronous?
Asynchronous: operations start at given conditions (when data ready or last processing is finished)
  Used for larger time windows
  Average latency (with large buffers to absorb fluctuations)
  If buffer size ≠ dead-time → lost events
  Used also for “software filters”
FE buffers
Local trigger
decision+timestamp
Global trigger decision back to the FE
FE data
to DAQ or clear
Take data when ready
YES/NO
data+timestamp
Average maximum time
  Pro’s: more resilient to data burst; running on conventional CPUs
  Con’s: needs a timing signal synchronised to the FE to latch the data, needs time-marker stored in the data, data transfer protocol is more complex)

## Slide 131: Synchronous or asynchronous? Why not both?
Pseudo-synchronous: operates locally phase-locked
  Data move in lockstep through the trigger chain from a set of local clocks
  Buffering required whenever you move between clocks
  Clocks run slightly faster than source data to prevent overflow
  Realignment to global clock only after the final trigger stage
  Fixed latency
  Pro’s: dead-time free (just few clock cycles to protect buffers), no need for expensive globally-distributed clock, simpler alignment procedure
  Con’s: must propagate timing info with data, buffering required to handle clock-domain change
T1
T4
T3
T2
Local
trigger decision
Global trigger decision going back to FE
FE data
to the DAQ
YES
data
Fixed time
FE buffers

## Slide 132: Conventional Architecture
Each subsystem is regionally segmented
Each region must talk to its neighbour
  This is the root cause of requiring specialized boards for a given task!
Each region of each processing layer compresses, suppresses, summarizes or otherwise reduces its data and passes it on to the next level which is less regionally segmented
Globally
laterally connected system
Detector data ordering
Many, many details on time-multiplexing and conventional architectures in sections 1-3 of https://cds.cern.ch/record/1421552/files/IN2011_022.pdf (although please note that the systems proposed in section 4-9 are very outdated and should be ignored)

## Slide 133: Time-multiplexed Architecture
Buffer data and stream it out optimized for processing
Spread processing over time
  Stream-processing rather than combinatorial-logic
  Maximise reuse of logic resources
  Easiest for FPGA design tools to route and meet timing
Costs you latency, bought back by more efficient processing
Detector data ordering
Self-contained
event processing nodes
Many, many details on time-multiplexing and conventional architectures in sections 1-3 of https://cds.cern.ch/record/1421552/files/IN2011_022.pdf (although please note that the systems proposed in section 4-9 are very outdated and should be ignored)

## Slide 134: High Level Trigger design principles
Offline reconstruction too slow to be used directly
  Takes >10s per event
  HLT usually needs << 1s
Instead, step-wise processing with early rejection
  Stop processing as soon as one step fails
  Event accepted if any of the trigger passes
  Add a time-out to kill the Poisson tail!
Fast reconstruction & L1-guided regional reconstruction first
Precision reconstruction as full detector data becomes available

## Slide 135: High Level Trigger design principles
Early rejection reduce data and resources (CPU, memory, etc.)
Event-level parallelism
  Process more events in parallel
  Multi-processing or/and multi-threading
Algorithm-level parallelism
  GPUs effective whenever large amount of data can be processed concurrently (although bandwidth can be a limiting factor)
Algorithms developed and optimized offline
Common HLT-reconstruction software framework reduces maintenance and increases reliability

## Slide 136: Example: CMS HLT
Approximately 38,000 cores
  An equal mix of Haswell, Broadwell and Skylake
Multithreading allows the cores to share non-event data
  Reduced memory footprint → can process more events: ~20% higher performance
  ATLAS currently doesn't have this: a race to implement this in ATHENA for Run 3
Upgrades to add a GPU in every filter farm node is ruled out by cost and power
  More likely a dedicated server sub-farm which does heavy tasks on demand
  FPGAs acceleration also a (possibly better) option

## Slide 137: Conclusion
Triggers are not new
  but they are constantly evolving as the accelerators and detectors do
FPGAs are the weapon of choice for the Level-1 trigger
  but they are not a magic bullet
The design of how you structure the transfer of data around your system is the most important decision you will make
Heterogeneous computing farms look likely to feature at HL-LHC
  but it is a brave new world!

## Slide 138: Conclusion
Triggers are not new
  but they are constantly evolving as the accelerators and detectors do
FPGAs are the weapon of choice for the Level-1 trigger
  but they are not a magic bullet
The design of how you structure the transfer of data around your system is the most important decision you will make
Heterogeneous computing farms look likely to feature at HL-LHC
  but it is a brave new world!
Oh, and be very suspicious if your supervisor plies you with strong coffee and gets you to look for scintillation light

## Slide 139: Spares: Introduction to FPGAs

## Slide 140: And this is not a new point
“The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue, this is a decided disadvantage”
Daniel Slotnick, 1967

## Slide 141: Field Programmable Gate Arrays
Programmable Logic Blocks
Massive Fabric of Programmable Interconnects
Notes: A field-programmable gate array (FPGA) is a large-scale integrated circuit that can be programmed after it is manufactured rather than being limited to a predetermined, unchangeable hardware function. The term "field-programmable" refers to the ability to change the operation of the device "in the field," while "gate array" is a somewhat dated reference to the basic internal architecture that makes this after-the-fact reprogramming possible.

## Slide 142: Combinatorial Logic Block
Registers on the output of every cell
Perfect for pipelined logic

## Slide 143: Integrated Digital Signal Processing
So many registers
Perfect for pipelined logic

## Slide 144: Biggest Xilinx “Ultrascale+” Devices
Upwards of 9million logic cells
  All clocked at up to 500MHz
  Up to O(1015) operations per second
Upwards of 12000 DSPs
All pipelined
Fully programmable
And we have a winner!

## Slide 145: Biggest Xilinx “Ultrascale+” Devices
Upwards of 9million logic cells
  All clocked at up to 500MHz
  Up to O(1015) operations per second
Upwards of 12000 DSPs
All pipelined
Fully programmable
And we have a winner!
So what is the catch?

## Slide 146: Biggest Xilinx “Ultrascale+” Devices
Upwards of 9million logic cells
  All clocked at up to 500MHz
  Up to O(1015) operations per second
Upwards of 12000 DSPs
All pipelined
Fully programmable
And we have a winner!
So what is the catch?
Incredibly hard to program efficiently
  Thinking in a parallel, pipelined-fashion is exceptionally difficult
  A handful of real experts in CMS
Efficient use depends on efficiently structured data
The chip is just the start – needs to be attached to something
You are also responsible for the infrastructure

## Slide 147: Spares: Phase-2

## Slide 148: Tracker
Inner Tracker (pixel) design to extend coverage to η ≃ 3.8
OT Si-sensors ≃ 200µm thick - 90/100µm pitch - 2.5/5cm strips
OT Si-sensors ≃ 200µm thick - 90/100µm pitch - 1.5 mm macro-pixels
IT Si-silicon sensors ≤ 150µm thickness - 50x50 to 25x100µm2

## Slide 149: Tracker
Inner Tracker (pixel) design to extend coverage to η ≃ 3.8
Outer Tracker design driven by ability to provide tracks at 40 MHz to L1-trigger
-

## Slide 150: Outer tracker 2S modules
2S Modules: Two-strip double-layers
~10k modules
42M channels
8 CBCs per side
Front End
Hybrid
Service Hybrid
CIC
1 per side
Double-Layer
Si Strip Detectors
DC-DC
Converter
LP-GBT &
Optical VTRx
10 cm
5 cm
127 Strips/CBC
Each 2S Module:
Sensor Area ~100 cm2
16 CBCs, each reading 254 strips
(127 from top & bottom sensors)
4064 Channels in total
Readout both L1 triggered data & Primitive trigger data
IC & RAL
CBC
Flex PCB Hybrid
500µm CF Support
CF Stiffener
Bridge
Silicon sensors
Inner
Outer
½ Module
~5,000 modules @ 10Gb/s + ~10,000 modules @ 5Gb/s = 100Tb/s = 395 EB/yr

## Slide 151: Outer tracker 2S modules: Do they work?
Upper Sensor
Lower Sensor
2× CBC2
Stub turn-on curve for 2CBC mini-module at FNAL test-beam

## Slide 152: Calorimeter Endcap design
3D shower topology and time resolution of ~30ps
Electromagnetic Endcap (EE)
  28 layers of Silicon sensors in W/Pb absorber (25 X0, 1.7λ)
Hadronic Endcap (EH)
  24 layers: 8 silicon + 16 silicon/scint. tiles at high/low η in stainless steel absorber (9λ)
600 m2, 25000 modules , of hexagonal 8” sensors ~6M channels of area 0.5 and 1 cm2
253 tonnes Total power at end of life = 160-180 kW @-30C
520m2 Scint. Tiles 2x2 and 5x5 cm2 + SiPM ~400k channels
Facing a MegaGray Dose
1016 cm-2 1MeV Neutron equivalent fluence

## Slide 153: Calorimeter Endcap modules
593 m2 of silicon
6M ch, 0.5 or 1 cm2 cell-size
21,660 modules (8” or 2x6” sensors)
92,000 front-end ASICS
9,670 modules @ 10Gb/s = 100Tb/s ≈ 395 EB/yr
(Trigger data only, L1 accepted data on separate fibres)

## Slide 154: Calorimeter Endcap modules: Do they work?

## Slide 155: What are the firmware challenges at Phase-II?
You mean, apart from the small matter of 300Tb/s of data?
So much data it has to be zero-suppressed
  No (or, at least, limited) geometric timing which can be utilized
  Variable data-volume
    Do you handle the worst case? Very inefficient
    Do you handle the average? How do you handle overflows?
We did such a good job at Phase-I, people have very high expectations…

## Slide 156: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting

## Slide 157: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding

## Slide 158: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap

## Slide 159: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap
Particle-flow