## Slide 1: Trigger and Data-Acquisition: Part I
UK Advanced Instrumentation Course 2024
Andrew W. Rose, Imperial College London
awr01@imperial.ac.uk

## Slide 2: Credits
These slides draw heavily from a long and distinguished heritage of slides drawing heavily from other people’s slides which drew heavily from other people’s slides, who…
  Some of these include Sioni Summers, Alessandro Thea, Alex Tapper, Dan Saunders, Georg Auzinger – thanks to them all!

## Slide 3: A (slightly unapologetic) apology
My examples are heavily biased towards the LHC and CMS
  It’s where my experience is, it is what I know
The boundary between Trigger and DAQ is blurry, and I tend to err to the Trigger side
  It’s where my experience is, it is what I know

## Slide 4: Science: The basics
Science is the art of knowing what to record, and when

## Slide 5: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building
And we want statistics, a lot of statistics
Ten orders of magnitude

## Slide 6: Unfortunately, Statistics requires data
The LHC’s 40MHz crossing rate and 2×1034 cm-2 s-1 luminosity was chosen to provide 2 billion interactions per second
Unfortunately, 40MHz on a 70 million channel tracker produces the equivalent of 25Pbit/s of data

## Slide 7: How much data???!
1× Home broadband
CMS Raw
CMS compressed
1,000,000× Home broadband
1,000× Home broadband
CMS tape-store

## Slide 8: Unfortunately, Statistics requires data
The LHC’s 40MHz crossing rate and 2×1034 cm-2 s-1 luminosity was chosen to provide 2 billion interactions per second
Unfortunately, 2×1034 cm-2 s-1 luminosity produces ~50 times more background in your detector than signal (if there is a signal at all), making selection tricky
  And every time the LHC improves its performance, this gets worse
Higgs -> 4μ
+30 MinBias

## Slide 9: Unfortunately, Statistics requires data
And it gets worse…
  In-time pile up: Same crossing different interactions
  At LHC, new events come every 25 ns
  Out-of-time pile up: Due to events from different crossings
  Need to identify the bunch crossing that a given event comes from
Superimpose

## Slide 10: Science: The basics
Enormous data rate at e.g. CMS:
40 MHz collision rate x 1-2 MB event size > 60 TB/s
  Can’t write this to tape & process it later!
Do we need to write it all to tape?
  Tiny cross sections for Higgs and new physics
Process each event, decide to accept/reject
Ten orders of magnitude

## Slide 11: Science: The basics
Enormous data rate at e.g. CMS:
40 MHz collision rate x 1-2 MB event size > 60 TB/s
  Can’t write this to tape & process it later!
Do we need to write it all to tape?
  Tiny cross sections for Higgs and new physics
Process each event, decide to accept/reject
  All online - can’t go back and fix it
  Don’t screw up!
Ten orders of magnitude

## Slide 12: Science: The basics
Enormous data rate at e.g. CMS:
40 MHz collision rate x 1-2 MB event size > 60 TB/s
  Can’t write this to tape & process it later!
Do we need to write it all to tape?
  Tiny cross sections for Higgs and new physics
Process each event, decide to accept/reject
  All online - can’t go back and fix it.
  Don’t screw up!
Ten orders of magnitude
  This is the art of Triggering

## Slide 13: Reminder
Trigger basic requirements
  Need high efficiency for selecting processes for physics analysis
  Need large reduction of rate from unwanted high-rate processes
  Robustness is essential
  Highly flexible, to react to changing conditions
  System must be affordable

## Slide 14: What’s on the (Trigger) menu today?
Historical systems
Simple triggers
Complex triggers
Modern triggers

## Slide 15: The earliest trigger
Cloud-chamber images recorded on film
Need some way to trigger the camera

## Slide 16: The earliest trigger
Cloud-chamber images recorded on film
Need some way to trigger the camera
Grad student
†Artist’s impression

## Slide 17: The earliest trigger
High efficiency? Nope – reflexes too slow
Large rate reduction? Better than nothing
Robustness? No – keep wanting sleep, coffee, toilet breaks, etc.
Highly flexible? Depends on the student
Affordable? Well that’s one thing in your favour, I suppose
Grad student
†Artist’s impression

## Slide 18: The earliest trigger
High efficiency? Nope – reflexes too slow
Large rate reduction? Better than nothing
Robustness? No – keep wanting sleep, coffee, toilet breaks, etc.
Highly flexible? Depends on the student
Affordable? Well that’s one thing in your favour, I suppose
Grad student
†Artist’s impression
  Although Rutherford & Geiger did note that “Strong coffee with a pinch of Strychnine” improved an assistant’s ability to spot scintillation light

## Slide 19: The earliest trigger
Blackett pioneered a technique to trigger the camera of cloud chambers (and got the Nobel prize for this and other work)
Just missed out on discovering the positron in 1932
Stevenson and Street used this to confirm the discovery of the muon in 1937
Trigger photo capture when Geiger counters 1,2,3, but not 4 record coincidental measurements

## Slide 20: The simplest trigger systems
Source: Use the signals from the Front-End of the detectors themselves
  Binary: tracking detectors (pixels, strips)
  Analog: tracking detectors, time of flight detectors, calorimeters, …
Front-End
Pre-amplifier
Amplifier

## Slide 21: The simplest trigger systems
Source: Use the signals from the Front-End of the detectors themselves
  Binary: tracking detectors (pixels, strips)
  Analog: tracking detectors, time of flight detectors, calorimeters, …
The most trivial trigger algorithm: Signal > Threshold
  Apply the lowest possible threshold
  Identify best compromise between hit efficiency and noise rate
Source
Trigger signal
Discriminator
Accept
Reject
Front-End
Pre-amplifier
Amplifier

## Slide 22: Detector signals characteristics
Leading edge
Trailing edge
Pulse width
  Limits the effective hit rate
  Must be adapted to the desired trigger rate
Time walk
  The threshold-crossing time depends on the signal amplitude
  Must be minimal in good trigger systems
Time walk can be suppressed by triggering on total signal fraction
  Applicable on same-shape input signals with different amplitude
  Useful for scintillator detectors and photomultipliers

## Slide 23: The constant fraction discriminator
  Attenuation + configurable delay applied before the discrimination determines tCFD
  If delay too short, the unit works as a normal discriminator since the output of the normal discriminator fires later than the CFD part
Input pulse
Delayed input pulse
Attenuated inverted input
Bipolar pulse
The output of the CFD fires when the bipolar pulse changes polarity
at t = tcfd
Signals with the same rising time, at a fraction f

## Slide 24: Trigger logic implementation
Once we are in the digital domain, all manipulations can be broken down to a Boolean operations
Combinatorial
  Summing, Decoders, Multiplexers,…
Sequential
  Flip-flops, Registers, Counters,…
AND
OR
NOT

## Slide 25: Trigger logic implementation
Once we are in the digital domain, all manipulations can be broken down to a Boolean operations
Combinatorial
  Summing, Decoders, Multiplexers,…
Sequential
  Flip-flops, Registers, Counters,…
AND
OR
NOT
Data propagates as a wave through the logic
Operations happen at well defined times and in a well defined order

## Slide 26: A simple trigger wants a simple system
A simple trigger system can start with a NIM crate
Common support for electronic modules
Standard impedance, connections, logic levels
  Watch out for negative voltage levels: Low = 0v, High = -0.8V

## Slide 27: A simple trigger wants a simple system
Digital Logic
CFD
Threshold Discriminator
Analogue Delay

## Slide 28: A simple trigger and DAQ system
discriminators
coincidence logic
Front-Ends
start
delays
Digitizers (ADC, TDC,….)
busy
Trigger system
&
ReadOut
FE
FE
FE
FE
Fast links
Detector
DAQ system

## Slide 29: Keyword: DeadTime
The key parameter in high speed trigger systems design
  The fraction of the acquisition time when no events can be recorded.
  Typically of the order of few %
  Reduces the overall system efficiency
Arises when a given processing step takes a finite amount of time
  Readout dead-time
  Trigger dead-time
  Operational dead-time

## Slide 30: Deadtime Example
Writing to disk or tape is much slow than accepting data into RAM
If you select an event and start writing it to disk, you cannot accept any more events until you finish writing, even if they are interesting

## Slide 31: Deadtime example
For input rate “Rin”, Readout rate “Rout”, and time taken to write to disk “Td”
Fraction of 1s “lost” to writing = Rout•Td
Event output rate Rout = (1-Rout•Td)•Rin
Rout(Hz)
Rin(Hz)
Td=1s
Td=2s
  for Td = 1s →max rate = 1Hz
IRREDUCIBLE!!!
Fraction of surviving events
To achieve high efficiency ⟹

## Slide 32: Deadtime
Writing to disk or tape is much slow than accepting data into RAM
If you select an event and start writing it to disk, you cannot accept any more events until you finish writing, even if they are interesting
Same principle applies to processing time
  For example, ADCs

## Slide 33: A simple trigger system: Deadtime
discriminators
coincidence logic
Front-Ends
start
delays
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADC

## Slide 34: A simple trigger system: Deadtime
Detector
discriminators
coincidence logic
Front-Ends
start
delays
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADC
If ADC is the critical step for deadtime, this is clearly a really bad plan

## Slide 35: A simple trigger system: Parallelism
Detector
discriminators
coincidence logic
Front-Ends
start
delays
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Much more sensible!
Potentially much more expensive!
  Independent readout and trigger paths, one for each sensor element
  Digitisation and DAQ processed in parallel (as much as affordable!)

## Slide 36: Keyword: Latency
discriminators
coincidence logic
Front-Ends
delays
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
  Latency: Time to form the trigger decision and distribute to the digitisers
Latency

## Slide 37: A simple trigger system: Latency
discriminators
coincidence logic
Front-Ends
delays
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
  Latency: Time to form the trigger decision and distribute to the digitisers
  Signals must be delayed until the trigger decision is available
  The more complex is the selection, the longer is the latency
Latency

## Slide 38: A simple trigger system: Latency
discriminators
coincidence logic
Front-Ends
delays
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Analogue delay-lines are a bit risky, don’t you think?
Especially for more than one channel
Latency

## Slide 39: A simple trigger system
discriminators
coincidence logic
Front-Ends
delays
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Latency
If the ADCs are the slow part, can we use the time more profitably?

## Slide 40: A simple trigger system: Pre-trigger
discriminators
coincidence logic
Front-Ends
start
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Pre-trigger
Start ADC
  Pre-Trigger stage: very fast indicator of some minimal activity in the detector
  Used to START the digitisers, with no delay
  The complex trigger decision comes later
If the ADCs are the slow part, can we use the time more profitably?

## Slide 41: A simple trigger system: Pre-trigger
discriminators
coincidence logic
Front-Ends
start
busy
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Pre-trigger
Start ADC
Assumes the digitization time is longer than the latency of the trigger system!
What if that is not true?

## Slide 42: A simple trigger system: Pre-trigger
discriminators
coincidence logic
Front-Ends
start
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Pre-trigger
Start ADC
Digital delay
A PIPELINE
Since each digitization takes a finite time
Can store the result of each digitization in RAM until trigger decision is made
Data Valid

## Slide 43: Simple trigger system: Bunched Colliders
discriminators
coincidence logic
start
Trigger system
&
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Front-Ends
We have a master-clock – the bunch-crossings themselves!
No need for a pre-trigger
Digital delay
A PIPELINE

## Slide 44: A Simple trigger system: Digital Triggers
start
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Front-Ends
Digital delay
A PIPELINE
Digital Trigger system

## Slide 45: A Simple trigger system: Digital Triggers
start
FE
FE
FE
FE
Fast links
ReadOut
Mux
ADCs
Front-Ends
Digital delay
A PIPELINE
Digital Trigger system
  This is the fundamental design behind all modern collider trigger-systems

## Slide 46: And finally: A philosophical question
If you only see what the trigger accepts, how do you know what you have thrown away?

## Slide 47: And finally: A philosophical question
If you only see what the trigger accepts, how do you know what you have thrown away?
A good trigger will also have so-called Minimum-bias or Zero-bias paths
  Zero-bias – accept a truly random sample of events (even “empty”)
  Minimum-bias – accept a random sample of crossings with collisions
Allows you to look at what your trigger tells you not to

## Slide 48: What about non-collider experiments?
"Always on" detectors – "events" could occur at any time - continuous read out
  But most of the time, nothing is happening
Signals may be localised to one portion of the detector - local read out
"Events" may have very different durations - few ms to 100s seconds (e.g. supernova)
"Video" data compared to LHC experiments’ "Photo" data
Want to capture data when something ‘interesting’ does happen, and suppress the rest
Everything I have said about deadtime, latency, min-bias paths, etc. still applies!

## Slide 49: See you on TUESday for part II!
Any questions?