## Slide 1: Trigger Happy
Andy Rose, Imperial College, London
awr01@imperial.ac.uk
www.hep.ph.ic.ac.uk/~awr01
The ongoing evolution of the CMS detector and its hardware trigger

## Slide 2: Overview
The CMS detector
What is triggering and how is it done at CMS?
What are the complicating factors in a hardware trigger and can we get around them?
The CMS phase-II upgrades and the challenges they pose
Mainly for the benefit of students for whom these may be new concepts – hopefully a useful recap for everyone else!

## Slide 3: The LHC: Large Hadron Collider
27km
8.6km
100m

## Slide 4: CMS vs. Atlas vs. Pevensey II
CMS
14,000 ton
ATLAS
7,000 ton

## Slide 5: The CMS detector

## Slide 6: The CMS detector

## Slide 7: The CMS detector

## Slide 8: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers

## Slide 9: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
≡ 40 TBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
Data rates before zero-suppression

## Slide 10: The CMS detector
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~80k PbWO4 Ecal Crystals
≡ 40 TBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
Data rates before zero-suppression

## Slide 11: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS Raw
CMS Zero-suppressed

## Slide 12: How do you store O(Pb/s) data?
For a very short time…
  3.2μs in CMS

## Slide 13: How do you store O(Pb/s) data?
Store raw data on detector for 3.2μs
Tape storage
Hardware processing
PC farm
10 Tb/s

## Slide 14: Muon Candidates: Join the dots

## Slide 15: Electron/Photon Candidates: Spikes

## Slide 16: Jet Candidates: A mess

## Slide 17: How do you store O(Pb/s) data?
Answer: You don’t! You have to throw most of it away!
Throw away 399/400
Throw away 997/1000
Store raw data on detector for 3.2μs
100kHz
Hardware processing
PC farm
10 Tb/s
Tape storage
300Hz
0.5GB/s
Worldwide LHC computing grid
“Physicists analysing data”
100 GB/s

## Slide 18: First observation of a 125GeV particle decaying to two photons

## Slide 19: First observation of a 125GeV particle decaying to two Z-bosons

## Slide 20: Congratulations – it’s a boson

## Slide 21: The CMS Level-1 trigger
Tape storage
Hardware processing
PC farm
Where the real fun is to be had :)

## Slide 22: A divergence of the CMS and Atlas triggers?
Up to 2015, the Atlas and CMS triggers were similar
  With the caveat that Atlas has three levels compared to CMS’s two levels
Both hardware triggers used the same architecture and were forced into similar design choices
In the Phase-1 shutdown, CMS – pushed by the UK – made changes to its trigger which started pushing the two experiments down different paths…

## Slide 23: The tyranny of the links

## Slide 24: The job of the trigger
The job of the trigger is to receive a vast amount of data from a diverse set of subsystems
Analyse it
  in a very short amount of time (~1μs)
Give a yes-no answer on whether an event should be discarded

## Slide 25: How much data can a board receive?
1 for parallel
8/10 for any serial
64/66 for “fast” serial
<200Mbit/s for parallel
Up to 25Gbit/s for serial (but limited by cost)
1 for serial links
12/24/48 for parallel optics
≤160 for parallel
For LHC, every board is synchronous and everything is processed “in-time”. This is fixed at 25ns.
Only “free” parameter

## Slide 26: The tyranny of the links
But remember…
  Parallel links need big connectors so bandwidth limited by space available on circuit board
  Serial links have a serialization/deserialization latency of 75ns
    And we only have ~1000ns for the level-1 trigger in total
Running at non-multiples of LHC clock adds realignment latency
But really, the killer problem is caused by the sheer volume of data…

## Slide 27: The tyranny of the links
Say that you have too much data and that you can’t receive enough bits to fit all data onto a single board
You can split processing across multiple boards
Except that you need to handle the boundaries!
Which means either
  Duplicating the data before it reaches your processing cards
  Sharing data between your processing cards
Both of which mean increasing the volume of data going to each board
So you need more links
So you need more boards
Which means more boundaries
Which means more sharing/duplicating
…

## Slide 28: The tyranny of the links
Restricted by technology available
Restricted by only feasible architecture
Restricted by available space
Question:
So, what can you do?
Imagine a “card” with 4 input links and up to 4 output links…
Answer:
Chose the best available technology you can and then throw out as much data as you can get away with until you satisfy your bit-limit

## Slide 29: The conventional architecture
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
3
3
3
3
3
3
3
3
3
3
3
3
3
3
3
3
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
Thrown away enough data now!
BX:1
BX:2
BX:3
BX:4

## Slide 30: Can the tyranny be broken?
Restricted by technology available
Restricted by only feasible architecture
Restricted by available space
Maybe it’s time to start questioning the received wisdom…
Imagine a “card” with 4 input links and up to 4 output links…
Can we increase ?
This requires a completely new architecture
In order that every BX is processed, we require as many processing “nodes” as the number of bunch-crossings the data is transmitted over

## Slide 31: The time-multiplexed architecture
Well… this doesn’t look like a great start – but we’ll come back to it in a minute…

## Slide 32: The time-multiplexed architecture
32
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
3
3
3
3
3
3
3
3
3
3
3
3
3
3
3
3
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
All data for 1bx from all regions in a single card!
Everything you need!
5
5
5
5
5
5
5
5
5
5
5
5
5
5
5
5
1
2
6
6
6
6
6
6
6
6
6
6
6
6
6
6
6
6
7
7
7
7
7
7
7
7
7
7
7
7
7
7
7
7
All data for 1bx from all regions in a single card!
Everything you need!
All data for 1bx from all regions in a single card!
Everything you need!
BX:1
BX:2
BX:3
BX:4
BX:5
BX:6
BX:7

## Slide 33: Can the tyranny be broken?
YES!
  Time-multiplexing means that your trigger systems are no-longer limited by the number of links into a board!
  No need to throw away data before processing (although if you can, why not…)
  Fewer boundaries means less data and fewer fibre for a given resolution
NO!
  Time-multiplexing means that you CAN (but don’t have to) have the raw data-rate throughout your system – this means more links than if you throw data away!

## Slide 34: What about that horrible patch panel?
Pay Molex to have a robot build it for you and pack it into a 2U rackmount box

## Slide 35: The advantages of time-multiplexing
Minimizes (or even eliminates) boundaries
  Most different board “species” in CMS can be traced back to the need to handle a particular choice of geometric division
  TMT means no specialization of hardware for a particular boundary handling situation
    “One-board-fits-all” design
    All specialization is in firmware – complete flexibility
Advantages claimed in 2011

## Slide 36: The advantages of time-multiplexing
No duplication of data needed
  Less hardware and fewer links for a given resolution
Data need only be thrown away by choice, not necessity
  Should allow better physics
Equality of data
  Without duplication, all data is equal
  Can easily add new input sources
    Scalability
Advantages claimed in 2011

## Slide 37: Is this really the case?
Run 0
Run 1
18 of 1 type
9 of 1 type
The proof of the pudding is in the eating: CMS has been running with a TM calo trigger since 2015

## Slide 38: Is this really the case?
Run 0
Run 1
Conventional
Time-multiplexed
18 of 1 type
9 of 1 type

## Slide 39: Is this really the case?
Run 0
Run 1
Conventional
Conventional

## Slide 40: Is this really the case?
Run 0
Run 1
18 of 1 type
9 of 1 type

## Slide 41: : A generic optical stream processor
950Gb/s in and 950Gb/s out
700,000 logic blocks @400MHz
Designed by G. Iles, J. Jones, A. Rose & S. Greenwood at IC
And it is laid out rationally and looks pretty

## Slide 42: A divergence of the CMS and Atlas triggers?
In CMS, time-multiplexing has allowed, and become synonymous with, generic hardware
  Possibly because of my own (extreme) philosophical stance toward simplifying and rationalising which drove me to evangelize/push both time-multiplexing and generic hardware upon CMS.
So much so that, for phase-II, UKCMS has a “common hardware” work-package to meet the needs of all its subsystems
In contrast to Atlas Phase-1 where the push has been towards very specialist boards
  eFEX, jFEX, gFEX, etc.

## Slide 43: Three neat time-multiplexing tricks

## Slide 44: Three neat time-multiplexing tricks
Within a TM node, can daisy-chain physical boards/FPGAs with enormous bandwidth

## Slide 45: Three neat time-multiplexing tricks
Same daisy-chaining technique applies equally when combining multiple systems with the same time-multiplexing period

## Slide 46: Three neat time-multiplexing tricks
Imagine a system with N nodes
We lose a node due to hardware failure
  In a conventional trigger losing a board means degrading (or losing!) every event!
  With TM, we lose 1 BX in N – a (inadvertent) trigger prescale!
But we have a final card up our sleeve!
For an additional 1/Nth of the cost we can have a spare node which we can switch in at run-time
  Efficiency restored!

## Slide 47: Phase-II

## Slide 48: Phase-II
| 1035 cm−2s−1 | average 200 events/BX |

## Slide 49: The CMS Detector after Phase-II
Upgrades relevant to triggering
New pixel layers
Tracking included in trigger
Full granularity Ecal included in trigger
Complete replacement of endcap Ecal & Hcal
30ps timing resolution
MIP timing layer
30ps timing resolution
New CSC electronics
New GEM layers
Replace HPD with SiPM in Barrel HCAL
Depth info into trigger
New Beampipe
Modified Magnet Yolk
…

## Slide 50: The CMS Detector after Phase-II
Upgrades relevant to triggering
New pixel layers
Tracking included in trigger
Full granularity Ecal included in trigger
Complete replacement of endcap Ecal & Hcal
30ps timing resolution
MIP timing layer
30ps timing resolution
New CSC electronics
New GEM layers
Replace HPD with SiPM in Barrel HCAL
Depth info into trigger
New Beampipe
Modified Magnet Yolk
…
Does anything remain?

## Slide 51: Tracker
Inner Tracker (pixel) design to extend coverage to η ≃ 3.8

## Slide 52: Tracker
Inner Tracker (pixel) design to extend coverage to η ≃ 3.8
OT Si-sensors ≃ 200µm thick - 90/100µm pitch - 2.5/5cm strips
OT Si-sensors ≃ 200µm thick - 90/100µm pitch - 1.5 mm macro-pixels
IT Si-silicon sensors ≤ 150µm thickness - 50x50 to 25x100µm2

## Slide 53: Tracker
Inner Tracker (pixel) design to extend coverage to η ≃ 3.8
Outer Tracker design driven by ability to provide tracks at 40 MHz to L1-trigger
-

## Slide 54: Outer tracker 2S modules
2S Modules: Two-strip double-layers
~10k modules
42M channels
8 CBCs per side
Front End
Hybrid
Service Hybrid
CIC
1 per side
Double-Layer
Si Strip Detectors
DC-DC
Converter
LP-GBT &
Optical VTRx
10 cm
5 cm
127 Strips/CBC
Each 2S Module:
Sensor Area ~100 cm2
16 CBCs, each reading 254 strips
(127 from top & bottom sensors)
4064 Channels in total
Readout both L1 triggered data & Primitive trigger data
IC & RAL
CBC
Flex PCB Hybrid
500µm CF Support
CF Stiffener
Bridge
Silicon sensors
Inner
Outer
½ Module

## Slide 55: Tracking Trigger
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
Tracking Trigger
~5,000 modules @ 10Gb/s + ~10,000 modules @ 5Gb/s = 100Tb/s = 394 EB/yr

## Slide 56: Outer tracker 2S modules: Do they work?
Upper Sensor
Lower Sensor
2× CBC2
Stub turn-on curve for 2CBC mini-module at FNAL test-beam

## Slide 57: Calorimeter Endcap design
3D shower topology and time resolution of ~30ps
Electromagnetic Endcap (EE)
  28 layers of Silicon sensors in W/Pb absorber (25 X0, 1.7λ)
Hadronic Endcap (EH)
  24 layers: 8 silicon + 16 silicon/scint. tiles at high/low η in stainless steel absorber (9λ)
600 m2, 25000 modules , of hexagonal 8” sensors ~6M channels of area 0.5 and 1 cm2
253 tonnes Total power at end of life = 160-180 kW @-30C
520m2 Scint. Tiles 2x2 and 5x5 cm2 + SiPM ~400k channels
Facing a MegaGray Dose
1016 cm-2 1MeV Neutron equivalent fluence

## Slide 58: Calorimeter Endcap modules
593 m2 of silicon
6M ch, 0.5 or 1 cm2 cell-size
21,660 modules (8” or 2x6” sensors)
92,000 front-end ASICS

## Slide 59: High-Granularity Endcap Calorimeters
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
HGcal
7,500 modules @ 10Gb/s = 75Tb/s ≈ 300 EB/yr
(Trigger data only, L1 accepted data on separate fibres)

## Slide 60: Calorimeter Endcap modules: Do they work?

## Slide 61: What are the firmware challenges at Phase-II?
You mean, apart from the small matter of 300Tb/s of data?
So much data it has to be zero-suppressed
  No (or, at least, limited) geometric timing which can be utilized
  Variable data-volume
    Do you handle the worst case? Very inefficient
    Do you handle the average? How do you handle overflows?
We did such a good job at Phase-I, people have very high expectations…

## Slide 62: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting

## Slide 63: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding

## Slide 64: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap

## Slide 65: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap
Particle-flow

## Slide 66: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap
Particle-flow
So, basically, they want event reconstruction

## Slide 67: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap
Particle-flow
So, basically, they want event reconstruction
  in under 10μs

## Slide 68: And we have stepped up to the plate!
I used to give the following firmware advice to my students on preserving their sanity:
  Avoid iterative algorithms
  Avoid combinatorics
  Make the data-flow deterministic
  Division is hard, resource hungry and latency intensive
  Floating-point is hard, resource hungry and latency intensive

## Slide 69: And we have stepped up to the plate!
For track fitter we wrote a full Kalman Filter
  Which is iterative
  Results in combinatorics
  Is data-dependent (pseudo-deterministic)
  Requires a division
  We also played with floating-point but dropped it in the final version
Forecast
Update
In
Out

## Slide 70: And we have stepped up to the plate!
Fits a 4-point track in 1.5μs
Matches offline floating-point resolution
200 events of TTbar+200PU
OPEN BLUE: floating-point CMSSW
CLOSED BLACK: Hardware capture

## Slide 71: UK Common hardware: Serenity
ATCA Development Platform
Next-generation generic optical-stream processor
Carrier Card provides the board services
Daughter Cards host data-processing FPGAs

## Slide 72: UK Common hardware: Serenity
Standard configuration. Provision for:
  2 × 72+72 links @ 25Gbps optical link
    3.6 + 3.6 Tbps
  64 links @ 25Gbps between DCs
    1.6 Tbps
Optional optical expansion:
  2 × 96+96 links @ 25Gbps optical link
    4.8 + 4.8 Tbps
  16 links @ 25Gbps between DCs
    0.4 Tbps
North
South
36+36 firefly
64 pairs, direction unspecified
36+36 firefly
36+36 firefly
36+36 firefly
24+24 “spare”
24+24 “spare”
QSFP
CPU

## Slide 73: UK Common hardware: Serenity
Freedom to choose your preferred family, package, generation, (vendor?)
Freedom to choose your balance of optical and electrical connectivity
Reduces financial risk since carrier (bulk of potential failure-modes) qualified before FPGAs (bulk of the cost) are fitted!
North
South
36+36 firefly
64 pairs, direction unspecified
36+36 firefly
36+36 firefly
36+36 firefly
24+24 “spare”
24+24 “spare”
QSFP
CPU

## Slide 74: Conclusion
Time-multiplexing reduces or eliminates the boundary-handling problems which plague conventional trigger architectures
CMS has successfully used time-multiplexing in the phase-1 upgrade of the calorimeter trigger
Time-multiplexing allows (or even encourages) the use of generic optical-stream processors

## Slide 75: Conclusion
The phase-2 upgrades and environment pose significant challenges to the hardware trigger
  Both intrinsic and expectational
UK stepping up to face the challenges!
Time-multiplexing and generic hardware playing a prominent role in phase-2 upgrades

## Slide 76: Bring on the future! Thanks for listening!
Any questions?

## Slide 77: The CMS detector