## Slide 1: Trigger Happy 2
Andy Rose, Imperial College, London
awr01@imperial.ac.uk
www.hep.ph.ic.ac.uk/~awr01
The ongoing evolution of the CMS Detector and its L1-Trigger

## Slide 2: Introduction
This is a sequel to my 2011 seminar “Trigger Happy: A light-hearted look at the seriously hard business of hardware triggering (and how we are trying to make it easier)”
  http://www.hep.ph.ic.ac.uk/~awr01/seminars/triggerhappy/TriggerHappy_v1.1.pptx
That talk:
  Honestly (brutally) assessed the shortcomings of the existing CMS trigger
  Lay out my glorious vision for the Phase-I upgrade of CMS trigger electronics
    Speaker’s prerogative when you gave me a seminar soapbox
  Parts of that vision came to pass, some parts didn’t
This talk will assess where CMS stands now, and what it faces after the Phase-II upgrades
  And I’ll lay out my new glorious vision
  Well… if you are a seminar soapbox again

## Slide 3: Where are we with the LHC again?

## Slide 4: Where are we with the LHC again?
Run 0
2008-2010
0.05 fb-1

## Slide 5: In the beginning…
Run 0
2008-2010
0.05 fb-1

## Slide 6: Run 1
Run 0
2008-2010
0.05 fb-1

## Slide 7: Recap
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers

## Slide 8: Recap
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers
× 40,000,000 measurements per second

## Slide 9: Recap
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~80k PbWO4 Ecal Crystals
≡ 40 TBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers

## Slide 10: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS Front-end

## Slide 11: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS Front-end
A man is too apt to forget that in this world he cannot have everything.
A choice is all that is left to him.
Carl W. Buechner

## Slide 12: CMS: Visualizing the big numbers
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
1 Eb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
4 YB/yr
CMS Front-end
CMS L1T input
A man is too apt to forget that in this world he cannot have everything.
A choice is all that is left to him.
Carl W. Buechner

## Slide 13: Runs 0 & 1: How we processed data
Many boards of many different types

## Slide 14: Runs 0 & 1: How we processed data
Most of which looked similar to this…

## Slide 15: Runs 0 & 1: How we processed data
In systems that looked like this…

## Slide 16: Runs 0 & 1: How we processed data
And like this…

## Slide 17: Runs 0 & 1: How we processed data
But sometimes it’s OK to be hideous if it works

## Slide 18: Runs 0 & 1: How we processed data
But sometimes it’s OK to be hideous if it works
Who am I kidding? Such an opinion is for Philistines. We should always be aiming to produce something OF BEAUTY

## Slide 19: The Prophecy and the Vision

## Slide 20: The Prophetic Witticism…
By 2015, every board in the [CMS] trigger will be identical and, after that, they will only get more similar
Andy Rose, 2010

## Slide 21: … which accompanied “The Vision”
In 2012, I presented my glorious vision:
Using time-multiplexing to achieve homogeneity by eliminating boundaries
A beautiful, highly homogeneous system
  Common hardware
  Common link-standards
  Common software for controlling everything

## Slide 22: The Vision
One board to rule them all, One link-standard to bind them, One control-bus to rule them all, And one software to mind them.

## Slide 23: The Vision
One board to rule them all, One link-standard to bind them, One control-bus to rule them all, And one software to mind them.

## Slide 24: The Prophetic Witticism
If you standardize the links and eliminate system-specific boundaries, then all boards
receive parallel streams of data
process parallel streams of data
output parallel streams of data
PCB
Large FPGA
Multi Gbit TX
Multi Gbit TX
Multi Gbit TX
Multi Gbit RX
Multi Gbit RX
Multi Gbit RX
RAM
RAM
DAQ and Control interface
Powering,
etc.

## Slide 25: : The original and the best
950Gb/s in and 950Gb/s out
700,000 logic blocks @400MHz
Designed by G. Iles, J. Jones, A. Rose & S. Greenwood at IC

## Slide 26: : The original and the best
950Gb/s in and 950Gb/s out
700,000 logic blocks @400MHz
Designed by G. Iles, J. Jones, A. Rose & S. Greenwood at IC
And it is laid out rationally and looks pretty

## Slide 27: The Prophetic Witticism
Couple the limited variation in the tasks with the fact that:
The reign of ASICs was over: Long live the FPGA
The number of vendors making sufficiently powerful FPGAs was limited
The number of vendors making sufficiently fast optics was also limited
And the logic behind the prophecy becomes obvious
PCB
Large FPGA
Multi Gbit TX
Multi Gbit TX
Multi Gbit TX
Multi Gbit RX
Multi Gbit RX
Multi Gbit RX
RAM
RAM
DAQ and Control interface
Powering,
etc.

## Slide 28: The Prophetic Witticism
Couple the limited variation in the tasks with the fact that:
The reign of ASICs was over: Long live the FPGA
The number of vendors making sufficiently powerful FPGAs was limited
The number of vendors making sufficiently fast optics was also limited
And the logic behind the prophecy becomes obvious, and so the prophecy came to pass…
PCB
Large FPGA
Multi Gbit TX
Multi Gbit TX
Multi Gbit TX
Multi Gbit RX
Multi Gbit RX
Multi Gbit RX
RAM
RAM
DAQ and Control interface
Powering,
etc.

## Slide 29: The Prophetic Witticism
CTP7
MTF7
(MTF6 shown)
TwinMux
CPPF
Virtex-7 690T
Avago Optics
Avago Optics
Avago Optics
Avago Optics
Avago Optics
Avago Optics
Avago Optics
Avago Optics
Virtex-7 690T
Virtex-7 690T
Virtex-7 690T

## Slide 30: The Vision vs. Reality
Runs 0 & 1
Run 2
Conventional
Time-multiplexed
18 of 1 type
9 of 1 type

## Slide 31: The Vision vs. Reality
Runs 0 & 1
Run 2
Conventional
Conventional

## Slide 32: The Vision vs. Reality
Runs 0 & 1
Run 2
18 of 1 type
9 of 1 type

## Slide 33: The Vision vs. Reality: Definitely better
“That is simple, my friend. It is because politics is more difficult than physics.”
Albert Einstein 1946

## Slide 34: An aside: The Firmware Operating System
MP7 achieved this by
  Separating the payload from the infrastructure
  Standardizing the interfaces
  Producing a build-tool to allow anyone to build their design in “unfamiliar hardware”
A victory for standardization!
DAQ
Control
SerDes & Buffers
SerDes & Buffers
Payload

## Slide 35: The Vision vs. Reality: Much, much better!

## Slide 36: The Vision vs. Reality: Ever so nearly perfect!
IPbus designed out the US
  Picked up at IC and bugs fixed
  V2 produced at IC/RAL/Bristol
  Adopted as standard across CMS
  Then in the LHC accelerator group, ATLAS, LHCb, Alice, XFEL, SoLid, ProtoDune…
uHAL software library written at IC
  Goes hand-in-hand with IPbus
Hurrah! A major victory for standardization!

## Slide 37: Phase 1: Conclusion
Time-multiplexing works
  Has been shown to offers all the benefits we said it would!
  Now well established in the CMS mindset
The prophecy that all off-detector electronics would be “identical” in 2015 came to pass
The run-2 trigger was certainly more elegant and robust than runs 0 & 1
Many UK-originated ideas gained traction outside the UK:
  Common hardware
  Firmware operating system
  Standardization of link protocols and control infrastructure

## Slide 38: Phase 2: A Brave New World

## Slide 39: Brave New World
Run 0
2008-2010
0.05 fb-1

## Slide 40: The CMS Detector after Phase-II
Upgrades relevant to triggering
New pixel layers
Tracking included in trigger
Full granularity Ecal included in trigger
Complete replacement of endcap Ecal & Hcal
30ps timing resolution
MIP timing layer
30ps timing resolution
New CSC electronics
New RPC/GEM layers
Replace HPD with SiPM in Barrel HCAL
Depth info into trigger
New Beampipe
Modified Magnet Yolk
…

## Slide 41: What’s the UK doing?
UK has led, and continues to lead, the development of the Stacked-tracker concept and the tracking-trigger
  UK delivering outer-tracker trigger and readout ASIC
  UK delivering outer-tracker readout-electronics and developing track-finding algorithms

## Slide 42: Tracker
Inner Tracker (pixel) design to extend coverage to η ≃ 3.8

## Slide 43: Tracker
Inner Tracker (pixel) design to extend coverage to η ≃ 3.8
OT Si-sensors ≃ 200µm thick - 90/100µm pitch - 2.5/5cm strips
OT Si-sensors ≃ 200µm thick - 90/100µm pitch - 1.5 mm macro-pixels
IT Si-silicon sensors ≤ 150µm thickness - 50x50 to 25x100µm2

## Slide 44: Tracker
Inner Tracker (pixel) design to extend coverage to η ≃ 3.8
Outer Tracker design driven by ability to provide tracks at 40 MHz to L1-trigger
-

## Slide 45: Outer tracker 2S modules
2S Modules: Two-strip double-layers
~10k modules
42M channels
8 CBCs per side
Front End
Hybrid
Service Hybrid
CIC
1 per side
Double-Layer
Si Strip Detectors
DC-DC
Converter
LP-GBT &
Optical VTRx
10 cm
5 cm
127 Strips/CBC
Each 2S Module:
Sensor Area ~100 cm2
16 CBCs, each reading 254 strips
(127 from top & bottom sensors)
4064 Channels in total
Readout both L1 triggered data & Primitive trigger data
IC & RAL
CBC
Flex PCB Hybrid
500µm CF Support
CF Stiffener
Bridge
Silicon sensors
Inner
Outer
½ Module

## Slide 46: Outer tracker 2S modules: Do they work?
Upper Sensor
Lower Sensor
2× CBC2
Stub turn-on curve for 2CBC mini-module at FNAL test-beam

## Slide 47: What’s the UK doing?
UK has led, and continues to lead, the development of the Stacked-tracker concept and the tracking-trigger
  UK delivering outer-tracker trigger and readout ASIC
  UK delivering outer-tracker readout-electronics and developing track-finding algorithms
UK has led, and continues to lead, the development of the HGC concept
  Off-detector electronics and algorithms primarily a UK responsibility

## Slide 48: Calorimeter Endcap design
3D shower topology and time resolution of ~30ps
Electromagnetic Endcap (EE)
  28 layers of Silicon sensors in W/Pb absorber (25 X0, 1.7λ)
Hadronic Endcap (EH)
  24 layers: 8 silicon + 16 silicon/scint. tiles at high/low η in stainless steel absorber (9λ)
600 m2, 25000 modules , of hexagonal 8” sensors ~6M channels of area 0.5 and 1 cm2
253 tonnes Total power at end of life = 160-180 kW @-30C
520m2 Scint. Tiles 2x2 and 5x5 cm2 + SiPM ~400k channels

## Slide 49: Calorimeter Endcap design
3D shower topology and time resolution of ~30ps
Electromagnetic Endcap (EE)
  28 layers of Silicon sensors in W/Pb absorber (25 X0, 1.7λ)
Hadronic Endcap (EH)
  24 layers: 8 silicon + 16 silicon/scint. tiles at high/low η in stainless steel absorber (9λ)
600 m2, 25000 modules , of hexagonal 8” sensors ~6M channels of area 0.5 and 1 cm2
253 tonnes Total power at end of life = 160-180 kW @-30C
520m2 Scint. Tiles 2x2 and 5x5 cm2 + SiPM ~400k channels
Facing a MegaGray Dose
1016 cm-2 1MeV Neutron equivalent fluence

## Slide 50: Calorimeter Endcap modules
593 m2 of silicon
6M ch, 0.5 or 1 cm2 cell-size
21,660 modules (8” or 2x6” sensors)
92,000 front-end ASICS

## Slide 51: Calorimeter Endcap modules: Do they work?

## Slide 52: What’s the UK doing?
UK has led, and continues to lead, the development of the Stacked-tracker concept and the tracking-trigger
  UK delivering outer-tracker trigger and readout ASIC
  UK delivering outer-tracker readout-electronics and developing track-finding algorithms
UK has led, and continues to lead, the development of the HGC concept
  Off-detector electronics and algorithms primarily a UK responsibility
UK has played leading role in the trigger electronics and algos, would like to continue to do so
Barrel-Muon trigger currently using UK hardware and keen to continue doing so in future
Global trigger currently using UK hardware (future TBD)
Good relationship with those responsible for designing the MTD back-end, they are proposing to use UK hardware

## Slide 53: What’s the UK doing?
UK has led, and continues to lead, the development of the Stacked-tracker concept and the tracking-trigger
  UK delivering outer-tracker trigger and readout ASIC
  UK delivering outer-tracker readout-electronics and developing track-finding algorithms
UK has led, and continues to lead, the development of the HGC concept
  Off-detector electronics and algorithms primarily a UK responsibility
UK has played leading role in the trigger, electronics and algos would like to continue to do so
Barrel-Muon trigger currently using UK hardware and keen to continue doing so in future
Global trigger currently using UK hardware (future TBD)
Good relationship with those responsible for designing the MTD back-end, they are proposing to use UK hardware
So… looking like UK has major hardware role to play in every system except
Barrel Calorimeter
Endcap Muons
Pixels

## Slide 54: What’s the UK doing?
UK has led, and continues to lead, the development of the Stacked-tracker concept and the tracking-trigger
  UK delivering outer-tracker trigger and readout ASIC
  UK delivering outer-tracker readout-electronics and developing track-finding algorithms
UK has led, and continues to lead, the development of the HGC concept
  Off-detector electronics and algorithms primarily a UK responsibility
UK has played leading role in the trigger electronics and algos, would like to continue to do so
Barrel-Muon trigger currently using UK hardware and keen to continue doing so in future
Global trigger currently using UK hardware (future TBD)
Good relationship with those responsible for designing the MTD back-end, they are proposing to use UK hardware
So… looking like UK has major hardware role to play in every system except
Barrel Calorimeter
Endcap Muons
Pixels
Not bad going for a collaboration of only 4 institutes

## Slide 55: What’s the UK doing?
UK has led, and continues to lead, the development of the Stacked-tracker concept and the tracking-trigger
  UK delivering outer-tracker trigger and readout ASIC
  UK delivering outer-tracker readout-electronics and developing track-finding algorithms
UK has led, and continues to lead, the development of the HGC concept
  Off-detector electronics and algorithms primarily a UK responsibility
UK has played leading role in the trigger electronics and algos, would like to continue to do so
Barrel-Muon trigger currently using UK hardware and keen to continue doing so in future
Global trigger currently using UK hardware (future TBD)
Good relationship with those responsible for designing the MTD back-end, they are proposing to use UK hardware

## Slide 56: So who is stupid enough to take on the task of designing hardware for so many disparate systems?

## Slide 57: So who is stupid enough to take on the task of designing hardware for so many disparate systems?

## Slide 58: Serenity
ATCA Development Platform
Next generation optical stream processor
Carrier Card provides the board services
Daughter Cards host data-processing FPGAs

## Slide 59: Serenity
Standard configuration. Provision for:
  2 × 72+72 links @ 25Gbps optical link
    3.6 + 3.6 Tbps
  64 links @ 25Gbps between DCs
    1.6 Tbps
Optional optical expansion:
  2 × 96+96 links @ 25Gbps optical link
    4.8 + 4.8 Tbps
  16 links @ 25Gbps between DCs
    0.4 Tbps
North
South
36+36 firefly
64 pairs, direction unspecified
36+36 firefly
36+36 firefly
36+36 firefly
24+24 “spare”
24+24 “spare”
QSFP
CPU

## Slide 60: Serenity
Freedom to choose your preferred family, package, generation, (vendor?)
Freedom to choose your balance of optical and electrical connectivity
Reduces financial risk since carrier (bulk of potential failure-modes) qualified before FPGAs (bulk of the cost) are fitted!
North
South
36+36 firefly
64 pairs, direction unspecified
36+36 firefly
36+36 firefly
36+36 firefly
24+24 “spare”
24+24 “spare”
QSFP
CPU

## Slide 61: Serenity: One board to rule them all?
48
48
48
48
HGC Trigger v1 (now disfavoured)

## Slide 62: Serenity: One board to rule them all?
36
36
36
36
36
36
36
36
HGC DAQ
HGC Trigger v2
Barrel Muon Processor?
48
48
48
48
HGC Trigger v1 (now disfavoured)

## Slide 63: Serenity: One board to rule them all?
36
36
36
36
36
36
36
36
HGC DAQ
HGC Trigger v2
Barrel Muon Processor?
48
48
48
48
HGC Trigger v1 (now disfavoured)
Outer Tracker DTC
MTD DTC?
The Pixel DTC we are not building for political reasons
13
36
24
13
36
24
36
24
36
24

## Slide 64: Serenity: One board to rule them all?
36
36
60
36
36
The track-finder processor we are not building for political reasons. Ooops.
36
36
36
36
36
36
36
36
HGC DAQ
HGC Trigger v2
Barrel Muon Processor?
48
48
48
48
HGC Trigger v1 (now disfavoured)
Outer Tracker DTC
MTD DTC?
The Pixel DTC we are not building for political reasons
13
36
24
13
36
24
36
24
36
24

## Slide 65: Serenity: One board to rule them all?
I would show how it fulfils the role of the trigger correlator
  If anyone could tell me what they require of the trigger correlator
I’ll be darned if they can come up with a scenario it can’t handle
?
?
?
?
?
?
?
?
?
?

## Slide 66: So is the prophecy coming true?
Institutes using the APx “family of boards” (Whatever that will end up meaning)
U.S. Tracker groups
U.S. Barrel Muons

## Slide 67: So is the prophecy coming true?
Not the U.S.:
Serenity

## Slide 68: So is the prophecy coming true?
APX
BCP
Pixel DTC
Barrel Muons
Track-finder
Or: How many boards does the US actually need?
Merging?

## Slide 69: And have you settled the architecture question yet?
Track-trigger
Endcap Calorimeter
Barrel Muons
Forward Hadron Calorimeter
Endcap Muons
Barrel Calorimeter
TPG
TPG
TPG
TPG
TPG
Correlator
Global Trigger

## Slide 70: And have you settled the architecture question yet? Most likely architecture
Conventional
Time-multiplexed
Track-trigger
Endcap Calorimeter
Barrel Muons
Forward Hadron Calorimeter
Endcap Muons
Barrel Calorimeter
TPG
TPG
TPG
TPG
TPG
Correlator
Global Trigger

## Slide 71: And have you settled the architecture question yet? Most likely architecture
Conventional
Time-multiplexed
Track-trigger
Endcap Calorimeter
Barrel Muons
Forward Hadron Calorimeter
Endcap Muons
Barrel Calorimeter
TPG
TPG
TPG
TPG
TPG
Correlator
Global Trigger
Regression, not progress 
Requiring ugly, specialized boards

## Slide 72: And have you settled the architecture question yet? Is this starting to look familiar?
Track-trigger
Endcap Calorimeter
Barrel Muons
Forward Hadron Calorimeter
Endcap Muons
Barrel Calorimeter
TPG
TPG
TPG
TPG
TPG
Correlator
Global Trigger

## Slide 73: Anyway…
Enough of the politics
Back to the interesting stuff!

## Slide 74: What are the firmware challenges at Phase-II?

## Slide 75: What are the firmware challenges at Phase-II?
You mean, apart from the small matter of 300Tb/s of data?

## Slide 76: What are the firmware challenges at Phase-II?
You mean, apart from the small matter of 300Tb/s of data?
So much data it has to be zero-suppressed
  No (or, at least, limited) geometric timing which can be utilized
  Variable data-volume
    Do you handle the worst case? Very inefficient
    Do you handle the average? How do you handle overflows?

## Slide 77: What are the firmware challenges at Phase-II?
You mean, apart from the small matter of 300Tb/s of data?
So much data it has to be zero-suppressed
  No (or, at least, limited) geometric timing which can be utilized
  Variable data-volume
    Do you handle the worst case? Very inefficient
    Do you handle the average? How do you handle overflows?
We did such a good job at Phase-I, people have very high expectations…

## Slide 78: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting

## Slide 79: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding

## Slide 80: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap

## Slide 81: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap
Particle-flow

## Slide 82: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap
Particle-flow
So, basically, they want event reconstruction

## Slide 83: What are the firmware challenges at Phase-II?
Real-time track-finding and fitting
Real-time vertex-finding
3D cluster-finding in endcap
Particle-flow
So, basically, they want event reconstruction
  in under 10μs

## Slide 84: What are the firmware challenges at Phase-II?
I used to give the following firmware advice to the students on preserving your sanity:
  Avoid iterative algorithms
  Avoid combinatorics
  Make the data-flow deterministic
  Division is hard, resource hungry and latency intensive
  Floating-point is hard, resource hungry and latency intensive

## Slide 85: And we have stepped up to the plate!
For track fitter we wrote a full Kalman Filter
  Which is iterative
  Results in combinatorics
  Is data-dependent (pseudo-deterministic)
  Requires a division
  We also played with floating-point but dropped it in the final version
Forecast
Update
In
Out

## Slide 86: And we have stepped up to the plate!
Fits a 4-point track in 1.5μs
Matches offline floating-point resolution
200 events of TTbar+200PU
OPEN BLUE: floating-point CMSSW
CLOSED BLACK: Hardware capture

## Slide 87: STOP PRESS!
UK claims crown for 1st Phase-2 algorithm in Phase-2 hardware
Real-time vertex-finding
  4% LUTS, ~2% RAM & DSPs in KU115 FPGA
  240MHZ clock
  TM-period + 20clk latency
Running in Serenity hardware

## Slide 88: Conclusion
UK has been very dominant in the phase-1 changes to the CMS off-detector electronics
  Hardware, System Architecture, Firmware & Control Software
  More elegant systems which are more robust, more performant and easier to maintain
UK-originated ideas gaining traction for phase 2
  Time-multiplexing
  Common hardware
  Infrastructure firmware
Phase-2 upgrades introduce a whole new set of detector and trigger challenges
  UK stepping up with state-of-the-art hardware and firmware solutions

## Slide 89: Bring on the future! Thanks for listening!
Any questions?